## Slide 1
AUTOMOTIVE ETHERNET
Foundations
OSI Model · IEEE 802 Family · Domain vs Zonal Architecture
OPEN Alliance SIG · TC10 Sleep/Wake · TC14 10BASE-T1S
2-Hour Technical Briefing
OSI Model
IEEE 802
Architecture
OPEN Alliance
TC10/TC14

## Slide 2
Agenda
Seven topics structured for a 2-hour delivery
01
OSI Seven-Layer Model
Conceptual framework — separating signalling, framing, routing, transport, application
02
IEEE 802 Family Structure
802.3 PHY/MAC vs 802.1 bridging, VLANs, TSN — the critical two-way split
03
Domain Architecture
Function-grouped ECUs, Ethernet backbones, IP-based modularity and software reuse
04
Zonal Architecture
Geography-first topology, shared Ethernet infrastructure, TSN becomes mandatory
05
OPEN Alliance SIG
Profiling IEEE Ethernet for vehicle-grade conformance and interoperability
06
TC10 — Sleep and Wake-Up
Partial networking, low-power states, fast and deterministic PHY wake
07
TC14 — 10BASE-T1S
Multidrop PLCA bus, automotive profile, conformance testing, TC10 interaction

## Slide 3
1
OSI Seven-Layer Model
The conceptual framework for reasoning about network communication

## Slide 4
The Seven OSI Layers
Lower layers move signals and frames · Upper layers move meaning and conversations
7
Application
Highest layer — closest to user or application function. Service interfaces.
6
Presentation
Data format, encoding, encryption — ensures readable data between systems.
5
Session
Manages data exchange between presentation-layer entities.
4
Transport
Reliable end-to-end communication — TCP/UDP, flow and error control.
3
Network
Connectivity and path selection between end systems — IP lives at this layer.
2
Data Link
Frame transport across a physical link — physical addressing (MAC). IEEE 802.3.
1
Physical
Signalling over the medium — electrical, mechanical, procedural. PHY.
Why OSI Matters
Separates functional concerns that would otherwise get conflated
A PHY issue (L1), a switch-queueing issue (L2), and an IP routing issue (L3) require different debugging approaches
IEEE 802.3 occupies Layers 1 and 2
IEEE 802.1 operates above Layer 2
SOME/IP sits at Layer 7 — a completely different debug domain
Lower layers: move signals, frames, packets
Upper layers: move meaning and structure

## Slide 5
OSI Mapping — 802.3 and 802.1
Ethernet discussions become tractable once you stop treating Ethernet as one undivided thing
IEEE 802.3 — Layers 1 & 2
Physical Layer (L1) 100BASE-T1, 1000BASE-T1, 10BASE-T1S Line coding, MDI, PLCA, AEC-Q100 grade PHY CISPR 25 Class 5 EMC compliance Data Link Layer (L2) MAC — frame format, addressing, CSMA/CD
MDIO management interface (MDC/MDIO)
MII, RGMII, SGMII — MAC-PHY interface
AutoNeg and link establishment
IEEE 802.1 — Above Layer 2
Bridging & Switching VLANs (802.1Q), STP/RSTP/MSTP Forwarding databases, port roles Time-Sensitive Networking (TSN) gPTP (802.1AS), TAS (802.1Qbv), CBS FRER (802.1CB), Stream reservation Security & Management MACsec (802.1AE), 802.1X port auth
YANG models, NETCONF/RESTCONF

## Slide 6
2
IEEE 802 Family Structure
802.3 Ethernet · 802.1 Bridging & TSN · The automotive two-way split

## Slide 7
The IEEE 802 Family
IEEE 802 = LAN/MAN Standards Committee — multiple working groups, each covering a different networking domain
802.3
Ethernet
Physical layer + MAC. All Ethernet speeds — 10 Mbit/s to 800 Gbit/s. Automotive: 10BASE-T1S, 100BASE-T1, 1000BASE-T1.
802.1
Bridging & TSN
Bridging, VLANs, TSN, MACsec, management. Everything above the Ethernet MAC. The architecture working group.
802.11
Wi-Fi (WLAN)
Wireless LAN. A separate media family from 802.3. V2X and in-vehicle Wi-Fi connectivity.
802.15
Wireless PAN
Short-range wireless: Bluetooth, Zigbee, UWB. Automotive: key fobs, TPMS, interior sensing.
802.2
LLC sublayer (hist.)
Logical Link Control — historical L2 service interface used with 802.3 and 802.11.

## Slide 8
802.3 vs 802.1 — When You Are on Each Side
Automotive engineers need both sides simultaneously — knowing which side you are on prevents layer-confusion during debug
IEEE 802.3 — You are here when…
IEEE 802.1 — You are here when…
Selecting a PHY: 100BASE-T1 or 1000BASE-T1
Investigating link-up failures or eye diagrams
Reading MDC/MDIO register maps
Understanding PLCA for 10BASE-T1S multidrop
Configuring MII / RGMII / SGMII
Measuring EMI to CISPR 25 Class 5
Designing VLAN segmentation: ADAS vs infotainment
Configuring TAS gate schedules for brake-by-wire
Setting up gPTP synchronisation across a backbone
Deploying FRER for safety-critical redundancy
Writing YANG/NETCONF for a central zone switch
Implementing MACsec for backbone encryption

## Slide 9
3
Domain Architecture
Functions grouped by responsibility · Ethernet backbone · IP software reuse

## Slide 10
Domain Architecture — Fundamentals
Functions grouped by domain · Domain controllers talk over Ethernet · IP enables software reuse across programs
Ethernet
Backbone
ADAS
Domain Ctrl
Infotainment
Domain Ctrl
Powertrain
Domain Ctrl
Body & Comfort
Domain Ctrl
Chassis
Domain Ctrl
Central Gateway
Functions grouped by domain
ADAS, infotainment, powertrain, body, chassis — each with its own domain controller.
Ethernet is the backbone
Domain controllers talk over Ethernet — not CAN or LIN. High bandwidth, IP-based.
IP = software reuse
Applications over IP → ECU code reused across car programs and model lines.
Scales across variants
Same architecture scales from entry-level to flagship within a model line.

## Slide 11
Three Phases of Vehicle Architecture
The evolution from function-specific wiring to geography-first Ethernet infrastructure
Traditional / Central GW
Many function-specific ECUs
Non-Ethernet links (CAN, LIN, FlexRay)
Ethernet only where bandwidth forced it
Point-to-point function wiring
Heavy wiring harness — one wire per signal
Gateway translates between bus protocols
Domain Architecture
Functions grouped by domain
Domain controllers on Ethernet backbone
Strong IP / software modularity
ECU code reused across car programs
Reduced gateway complexity
Current OEM focus (per IEEE use-case doc)
Zonal Architecture
Physical zones = primary organiser
Many functions share one Ethernet backbone
TSN + Ethernet switching mandatory
Smaller, lighter wiring harness
Better OTA update support
Same topology reused across variants

## Slide 12
4
Zonal Architecture
Geography-first · Shared Ethernet backbone · TSN as a hard requirement

## Slide 13
Zonal Architecture — What Changes
Grouping principle shifts from function to physical location — zone controllers aggregate all nearby ECUs
Ethernet
Backbone (TSN)
Front Left
Zone Ctrl
Front Right
Zone Ctrl
Central
Compute
Rear Left
Zone Ctrl
Rear Right
Zone Ctrl
↓ Harness weight & cost
Fewer long runs — zone controllers aggregate local ECUs over short cable runs
Any data, anywhere
Shared Ethernet backbone — no dedicated point-to-point runs between domains
OTA update friendly
Software delivered centrally over Ethernet — no physical access to each ECU
Requires TSN expertise
VLANs, TAS, gPTP, FRER all become mandatory — deep 802.1Q skills required

## Slide 14
Zonal Architecture — IEEE Stated Drivers
From the IEEE automotive use-case document — quantified trends and explicit requirements
"Zonal networks are seen by many as the flexible networking solution. Ethernet's scalable bandwidth and TSN capabilities become requirements here, on top of the OSI layering and IP addressing that domain networks introduced."
Harness Reduction
Wiring harness size, weight, cost, and complexity all decrease.
Topology Freedom
Any data can flow anywhere without unnecessary dedicated links.
OTA Update Support
Software updates delivered centrally over the backbone.
Architecture Reuse
Same zone topology scales across low-, mid-, high-end variants.
TSN Redundancy
Easier FRER deployment when all ECUs share the backbone.
Deep Ethernet Skills
VLANs, TSN, gPTP, MACsec — the full 802.1Q stack becomes mandatory.

## Slide 15
5
OPEN Alliance SIG
Profiling IEEE Ethernet for automotive-grade implementation

## Slide 16
OPEN Alliance SIG — Role and Purpose
Not a replacement for IEEE — a profiling and industrialization layer on top of IEEE Ethernet standards
IEEE 802.3 + IEEE 802.1
Base Ethernet and TSN Standards
OPEN Alliance SIG
Implementation · Conformance · Interoperability · Sleep/Wake profiles
Automotive-Ready Product
OEM-deployable, certified, interoperable Ethernet nodes
Multi-speed specs
Covers 10BASE-T1S, 100BASE-T1, 1000BASE-T1 — all automotive speed grades
Implementation specs
Turn abstract IEEE requirements into concrete automotive design guidance
Conformance testing
TC14 compliance specs: labs can certify 'this PHY meets the automotive profile'
Interoperability
Interop events test multi-vendor coexistence on the same physical bus
Sleep/wake specs
TC10: how automotive PHYs enter and exit low-power states
Joint working groups
TC10/TC14 joint WG: 10BASE-T1S sleep/wake on a multidrop bus

## Slide 17
6
TC10 — Sleep and Wake-Up
Automotive PHY power management · Partial networking · Fast deterministic wake

## Slide 18
TC10 — Sleep / Wake-Up Specification
Unlike an office switch, an automotive Ethernet node must sleep, wake on demand, and support partial networking
ACTIVE
Full operational
Ethernet link
STANDBY
Reduced power
wake-capable
SLEEP
PHY powered
down
WAKE
Transition
state
sleep cmd
wake cmd
xMII family compatible
Works across MII, RMII, RGMII, SGMII — no proprietary side-channels needed
Multi-speed support
Covers 10BASE-T1S, 100BASE-T1, 1000BASE-T1 across all automotive speeds
Partial networking
Individual links sleep while others remain active — not all-on or all-off
Fast deterministic wake
Network must be operational within the vehicle wake-sequence time budget
Active standardisation
Updated TC10 electrical interface spec published 2025 — still evolving

## Slide 19
7
TC14 — 10BASE-T1S in Automotive
Multidrop · PLCA · Conformance testing · Interoperability

## Slide 20
TC14 — 10BASE-T1S Automotive Enablement
10BASE-T1S is not just another PHY — it is a multidrop bus replacing CAN in low-bandwidth in-vehicle networks
Topology
Multidrop — up to 8 nodes share one bus segment without a switch
Speed
10 Mbit/s — sufficient for body, sensor, and low-bandwidth control
Media access
PLCA (Physical Layer Collision Avoidance) — deterministic round-robin
Cable
Unshielded single twisted pair — halves wiring cost vs point-to-point
Power
Optional PoDL (Power over Data Line) — sensor powering on the same pair
Profile
OPEN Alliance TC14: automotive-grade EMC, temperature, compliance testing
System impl spec
Translates abstract IEEE 802.3cg requirements into concrete automotive design rules
Conformance testing
Compliance specs verify PHY characteristics against the automotive profile
Interop events
Regular events test multi-vendor coexistence on the same 10BASE-T1S bus segment
TC10 joint work
TC14/TC10 Joint WG produced the 10BASE-T1S Sleep/Wake specification
Ecosystem answer
TC14 lets industry answer: 'Does this 10BASE-T1S PHY work in an automotive vehicle?'

## Slide 21
TC10 and TC14 — A Coordinated Ecosystem
Real automotive Ethernet standardisation is not isolated documents — it is a coordinated ecosystem
TC10
Sleep/Wake
TC14
10BASE-T1S
JOINT
WG
· xMII sleep/wake signalling
· 100BASE-T1 sleep spec
· 1000BASE-T1 sleep spec
· 10BASE-T1S system impl
· Conformance test suite
· EMC & temp profiles
· 10BASE-T1S Sleep/Wake
· Multidrop partial net.
Key insight
IEEE gives you the broad networking language.
OPEN Alliance makes it vehicle-ready through implementation specs, conformance testing, and interoperability events.
TC10 and TC14 collaborate directly — the 10BASE-T1S sleep/wake spec is a joint working group deliverable.

## Slide 22
The Complete Picture
How all six topics integrate into a coherent automotive Ethernet understanding
OSI Model
Separates signalling, framing, routing, transport, and application — prevents layer confusion during engineering and debug sessions.
IEEE 802 Family
802.3 owns L1+L2 (PHY and MAC). 802.1 owns bridging, VLANs, TSN, and security. Knowing which side prevents misdiagnosis.
Domain → Zonal
Architecture driven by bandwidth, OTA, harness cost, and software reuse. Ethernet and TSN shift from optional to mandatory.
OPEN Alliance SIG
Profiles IEEE Ethernet into automotive-grade specs. Implementation guides, conformance testing, and interoperability events.
TC10 Sleep/Wake
Automotive PHYs must sleep, partially network, and wake deterministically. TC10 specifies this across all speeds.
TC14 10BASE-T1S
Multidrop, PLCA, automotive profile. TC14 ensures the industry can manufacture and validate compatible devices.

## Slide 23
Questions &
Discussion
OSI Model — Conceptual layering for Ethernet reasoning
IEEE 802.3 + 802.1 — PHY/MAC vs bridging/TSN
Domain Architecture — Function-first, Ethernet backbone, IP reuse
Zonal Architecture — Geography-first, shared backbone, TSN mandatory
OPEN Alliance — IEEE profiling for automotive grade
TC10 + TC14 — Sleep/wake and 10BASE-T1S conformance