## Slide 1
Automotive Ethernet
Architecture, Standards & OPEN Alliance SIG
Training Session — 2 Hours
CONFIDENTIAL — Internal Use Only

## Slide 2
Session agenda
0:00 – 0:30
Zonal vs domain vehicle architecture
E/E architecture evolution, trade-offs, OEM adoption
0:30 – 0:55
OSI 7-layer model
Layer responsibilities, automotive protocol mapping
0:55 – 1:20
IEEE 802 family structure
802.3 Ethernet, 802.1 bridging, automotive PHY standards
1:20 – 1:50
OPEN Alliance SIG
TC10 sleep/wake, TC14 two-pair Ethernet, ecosystem role
1:50 – 2:00
Summary & Q/A
Key takeaways, further reading

## Slide 3
01
Zonal vs domain
vehicle architecture
E/E architecture evolution • 30 minutes

## Slide 4
E/E architecture evolution
2000s
Discrete ECUs
Point-to-point wiring
70–100+ ECUs
CAN/LIN buses
2010s
Domain arch.
Domain controllers
Functional grouping
Gateway ECU
2020s
Zonal arch.
Zone controllers
Location-based
Central compute
Future
Vehicle computer
Single HPC
Software-defined
Cloud-native
Key driver: reducing wiring harness weight (30–50 kg) and enabling software-defined vehicle (SDV) platforms
Notes: The evolution of vehicle E/E architecture is driven by two primary forces: reducing physical complexity (wiring harness weight and cost) and enabling software-defined vehicles. Modern premium vehicles have 70-100+ ECUs interconnected by kilometres of wiring. The move from discrete ECUs to domain architecture grouped ECUs by function (powertrain, chassis, ADAS, body, infotainment). Zonal architecture groups by physical location instead, with zone controllers acting as local aggregation points that connect to central high-performance computers via high-bandwidth Ethernet backbone.

## Slide 5
Domain architecture
ECUs grouped by function — each domain has a dedicated controller
Central gateway ECU
Powertrain
Domain Ctrl
Chassis
Domain Ctrl
ADAS
Domain Ctrl
Body
Domain Ctrl
Infotainment
Domain Ctrl
Engine
Mgmt
Trans
Ctrl
EMS
ABS
ESC
Susp
Ctrl
Radar
Camera
Lidar
BCM
Door
Ctrl
Lights
HU
Cluster
TCU
CAN / LIN / FlexRay sub-networks within each domain
Notes: In domain architecture, ECUs are grouped by functional domain. Each domain has a powerful domain controller that aggregates and processes data from its sub-ECUs. The central gateway routes inter-domain traffic. Limitations: (1) wiring still follows function, not proximity — a body ECU in the rear and one in the front both connect back to the body domain controller, requiring long cable runs. (2) Adding cross-domain features (e.g. ADAS using body sensors) requires inter-domain communication through the gateway, adding latency. (3) The gateway becomes a bottleneck as bandwidth demands grow.

## Slide 6
Zonal architecture
ECUs grouped by physical location — zone controllers connect to central compute
Central HPC / Vehicle Computer
ADAS • Infotainment • Body • Vehicle dynamics
Front-left
Zone Ctrl
Front-right
Zone Ctrl
Rear-left
Zone Ctrl
Rear-right
Zone Ctrl
Ethernet backbone (1G / 10G)
Headlamp
Radar
Wiper
Headlamp
Camera
Sensor
Taillight
Sensor
Motor
Taillight
Sensor
Trunk
Short local wiring (CAN/LIN/Ethernet) to nearest zone controller
Notes: In zonal architecture, ECUs are grouped by physical proximity — all sensors and actuators in the front-left of the vehicle connect to the front-left zone controller, regardless of their functional domain. Zone controllers aggregate local I/O and communicate with the central high-performance computer over a high-bandwidth Ethernet backbone (typically 1 Gbps or 10 Gbps). Benefits: (1) dramatically shorter cable runs — sensors connect to the nearest zone controller, reducing harness weight by 20-30%. (2) Cross-domain features are handled in the central compute, eliminating gateway bottlenecks. (3) Software updates can be deployed centrally. Examples: VW MEB/SSP platform, BMW Neue Klasse, Mercedes-Benz MB.OS.

## Slide 7
Domain vs zonal — comparison
Criterion | Domain architecture | Zonal architecture
Grouping principle | By function (powertrain, chassis, ADAS...) | By location (front-left, rear-right...)
Wiring harness | Long runs across vehicle (30–50 kg) | Short local runs (20–30% lighter)
Central compute | Gateway + domain controllers | HPC / vehicle computer
Cross-domain features | Inter-domain via gateway (added latency) | Central compute handles all (lower latency)
Software update | Per-domain OTA | Centralised OTA
Scalability | New domain = new controller | Scales via Ethernet bandwidth
OEM examples | Current-gen BMW, Toyota | VW SSP, BMW Neue Klasse, Mercedes MB.OS
Notes: Walk through each comparison row. Emphasise that zonal is not universally better — it requires a mature software platform (hypervisor, AUTOSAR Adaptive, SOA middleware) and high-bandwidth Ethernet backbone. Domain architecture is simpler for incremental evolution. The transition is driven by SDV requirements and wiring cost pressure. Many OEMs are in a hybrid phase with partial zonal implementation.

## Slide 8
Key takeaway
Zonal architecture is an Ethernet-first design.
The backbone between zone controllers and the central HPC is Ethernet — 100BASE-T1, 1000BASE-T1, and increasingly Multi-Gig (2.5G/5G/10G). This makes automotive Ethernet standards (IEEE 802.3, OPEN Alliance specifications) the enabling technology for the architectural transition.
100M+
Automotive Ethernet
ports shipped/year
30%
Harness weight
reduction target
10 Gbps
Backbone bandwidth
(zonal backbone)

## Slide 9
02
OSI 7-layer model
Protocol layering and automotive mapping • 25 minutes

## Slide 10
OSI reference model
7
Application
SOME/IP, DoIP, HTTP, DDS
6
Presentation
Serialisation, TLS, IDL
5
Session
SOME/IP-SD, Socket mgmt
4
Transport
TCP, UDP
3
Network
IPv4, IPv6, ARP, ICMP
2
Data link
Ethernet MAC (802.3), VLAN (802.1Q)
1
Physical
100BASE-T1, 1000BASE-T1, xMII
Upper
layers
IEEE 802
scope
Notes: The OSI model provides the conceptual framework. In automotive Ethernet, the key mapping is: Layer 1 = automotive PHY standards (100BASE-T1, 1000BASE-T1 — single twisted pair), Layer 2 = standard Ethernet MAC per IEEE 802.3 plus VLANs (802.1Q) and time-sensitive networking (802.1AS, 802.1Qbv), Layer 3 = standard IPv4/v6, Layer 4 = TCP/UDP, and the upper layers use automotive-specific protocols: SOME/IP for service-oriented communication, DoIP for diagnostics, SOME/IP-SD for service discovery. Note that IEEE 802 only covers Layers 1 and 2 — the MAC sublayer and the PHY.

## Slide 11
OSI layers in the automotive stack
Application (L7)
SOME/IP
DoIP (ISO 13400)
Service-oriented communication / Diagnostics over IP
Transport (L4)
UDP
TCP
SOME/IP typically over UDP; DoIP over TCP
Network (L3)
IPv4 / IPv6
ARP / ICMP
Standard IP networking — AUTOSAR provides the TCP/IP stack
Data link (L2)
Ethernet MAC
802.1Q VLAN
802.1AS (gPTP)
802.1Qbv (TAS)
MAC framing + time-sensitive networking extensions
Physical (L1)
100BASE-T1
(BroadR-Reach)
1000BASE-T1
(Multi-Gig)
Single unshielded twisted pair — automotive-specific PHY
Notes: Walk through the automotive protocol stack from bottom to top. Key points: (1) At L1, automotive Ethernet uses single unshielded twisted pair (UTP) instead of the 4-pair cables used in IT Ethernet — this is critical for weight and cost. 100BASE-T1 (IEEE 802.3bw) and 1000BASE-T1 (IEEE 802.3bp) are the primary automotive PHY standards. (2) At L2, time-sensitive networking (TSN) extensions like 802.1AS (generalised PTP for time synchronisation) and 802.1Qbv (time-aware shaper for scheduled traffic) are essential for mixing ADAS real-time traffic with infotainment best-effort traffic on the same Ethernet backbone. (3) SOME/IP is the dominant automotive middleware — it enables service-oriented architecture where ECUs discover and subscribe to services dynamically.

## Slide 12
03
IEEE 802 family
structure
Ethernet, bridging, and automotive PHY standards • 25 minutes

## Slide 13
IEEE 802 family structure
IEEE 802 defines LAN/MAN standards — Layers 1 and 2 of the OSI model
IEEE 802 — LAN/MAN Standards
802.1
Bridging
& Mgmt
802.3
Ethernet
802.11
Wi-Fi
802.15
WPAN
(BLE, Zigbee)
802.1Q
VLAN
Tagging
802.1AS
Time
Sync
Automotive-relevant standards highlighted
IEEE 802.3 — automotive Ethernet PHY standards
Standard | Speed | PHY name | Cable | Year
802.3bw | 100 Mbps | 100BASE-T1 | 1 UTP | 2015
802.3bp | 1 Gbps | 1000BASE-T1 | 1 UTP | 2016
802.3ch | 2.5/5/10G | MultiGBASE-T1 | 1 STP | 2020
802.3cg | 10 Mbps | 10BASE-T1S/T1L | 1 UTP | 2019
Notes: IEEE 802 is the umbrella for all LAN/MAN standards. For automotive, the critical working groups are: 802.3 (Ethernet) — especially the automotive PHY amendments: 802.3bw (100BASE-T1), 802.3bp (1000BASE-T1), 802.3ch (multi-gigabit), and 802.3cg (10 Mbps for low-cost sensor networks). 802.1 (bridging) — especially 802.1Q (VLANs for traffic segregation), 802.1AS (generalised precision time protocol for synchronisation across the vehicle), and 802.1Qbv (time-aware shaper for deterministic scheduling). The key difference from IT Ethernet: automotive uses single twisted pair (not 4-pair Cat5/6), operates in harsh EMC environments, and requires very low latency for safety-critical ADAS traffic.

## Slide 14
802.3 frame and 802.1 extensions
IEEE 802.3 Ethernet frame
Pre
7B
SFD
1B
Dst MAC
6B
Src MAC
6B
Type
2B
Payload (46–1500 bytes)
FCS
4B
802.1Q VLAN-tagged frame (4-byte tag inserted after Src MAC)
Dst MAC
6B
Src MAC
6B
TPID
0x8100
TCI
(PCP+VID)
Type
2B
Payload
FCS
4B
Key 802.1 TSN extensions for automotive
802.1AS
gPTP
Generalised precision time protocol — synchronises all nodes to a common time base (<1 µs accuracy). Essential for sensor fusion in ADAS.
802.1Qbv
TAS
Time-aware shaper — opens/closes traffic gates on a schedule so critical frames get guaranteed latency. Enables mixing ADAS and infotainment traffic.
802.1Qci
PSFP
Per-stream filtering and policing — enforces bandwidth and burst limits per traffic stream. Prevents a misbehaving ECU from flooding the network.
802.1CB
FRER
Frame replication and elimination — sends duplicate frames over disjoint paths for fault tolerance. Used in safety-critical ADAS communication.
Notes: Two key concepts to emphasise: (1) The 802.1Q VLAN tag adds 4 bytes after the source MAC address. The Tag Control Information (TCI) contains the 3-bit Priority Code Point (PCP) for QoS and the 12-bit VLAN ID. In automotive, VLANs segregate traffic domains — ADAS traffic on one VLAN, infotainment on another, diagnostics on a third. (2) TSN extensions are what make Ethernet viable for automotive real-time: 802.1AS provides sub-microsecond time synchronisation across all switches and endpoints, and 802.1Qbv uses this shared time base to schedule gate open/close windows, guaranteeing worst-case latency for critical traffic.

## Slide 15
04
OPEN Alliance SIG
TC10 & TC14
Industry consortium role, sleep/wake, two-pair Ethernet • 30 minutes

## Slide 16
OPEN Alliance SIG — role and structure
One-Pair Ether-Net — industry consortium driving automotive Ethernet adoption
What OPEN Alliance does
Defines interoperability specifications that complement IEEE/ISO standards:
Compliance test specifications
PHY-level interoperability requirements
Sleep/wake behaviour (TC10)
Connector & cabling specs (TC2)
EMC test specifications
Link segment models
Key technical committees
TC1
100BASE-T1 compliance
TC2
Connector specifications
TC6
MDI ( xMII) 10BASE-T1x MAC-PHY SPI
TC8
EMC test specifications
TC9
1000BASE-T1 compliance
TC10
Sleep/wake (energy mgmt)
TC12
1000BASE-T1 interop
TC14
10BASE-T1S (Multidrop)
Members include: BMW, Continental, Marvell, NXP, Broadcom, TI, Bosch, Qualcomm, and 300+ others
Notes: OPEN Alliance SIG (Special Interest Group) was founded in 2011 to promote automotive Ethernet adoption. The name stands for 'One-Pair Ether-Net'. Its role is NOT to create new standards (that's IEEE's job) but to define the interoperability, compliance testing, and application-level specifications that IEEE does not cover. For example, IEEE 802.3bw defines the 100BASE-T1 PHY electrically, but OPEN Alliance TC1 defines the compliance test procedure that PHY vendors must pass. Similarly, IEEE does not define sleep/wake behaviour for Ethernet (it's always-on by default) — TC10 fills this gap for automotive where energy management is critical. TC14 addresses the need for multi-gigabit over two pairs, beyond what 802.3ch single-pair covers.

## Slide 17
TC10 — sleep / wake for automotive Ethernet
Why TC10 exists
Standard Ethernet has no concept of sleep — the PHY link is always up and consuming power. In a vehicle with 20+ Ethernet ports, this wastes significant standby current. TC10 defines how an Ethernet link can enter and exit a low-power sleep state while maintaining the ability to wake on network activity.
TC10 link state machine
ACTIVE
Link up, data
transfer
SLEEP REQ
Coordinated
shutdown
SLEEP
PHY powered
down, <1 mW
WAKE
Wake pulse
detected
Link re-established
Key TC10 mechanisms
Sleep request:
MAC sends LPI (Low Power Idle) signalling via the MDIO interface, then PHY transitions to sleep
Wake forward:
A sleeping PHY can detect a wake pulse from the link partner and forward it to the local MAC
Wake sources:
Local wake (from MCU/hardware pin) or remote wake (from link partner's wake pulse on the wire)
Timing:
Wake-up latency typically <100 ms for 100BASE-T1, PHY must be ready to receive within spec'd time
Notes: TC10 is one of the most practically important OPEN Alliance specifications. In CAN networks, energy management is simple — the CAN transceiver has built-in selective wake (ISO 11898-2:2016) where a specific frame pattern on the bus wakes the node. Ethernet has no equivalent — IEEE 802.3az (EEE) reduces power during idle periods but doesn't truly sleep the PHY. TC10 defines: (1) a coordinated sleep handshake between MAC and PHY, (2) the PHY's ability to detect a specific wake pulse pattern on the twisted pair even while asleep, (3) the PHY's ability to forward wake events between the local host and the remote link partner. This is essential for partial networking — only the ECUs needed for a particular function wake up, while the rest remain in sleep, keeping vehicle standby current within the 12V battery budget.

## Slide 18
TC14 — two-pair automotive Ethernet
Why TC14 exists
802.3ch defines multi-gigabit over a single shielded twisted pair (STP), but automotive OEMs also need multi-gigabit over two unshielded pairs (UTP) for longer reach and lower cost. TC14 specifies the physical layer, cabling, and connector requirements for 2.5G/5G/10G Ethernet over two-pair UTP in the vehicle.
Single-pair vs two-pair comparison
 | Single-pair (802.3ch) | Two-pair (TC14 scope)
Speed | 2.5 / 5 / 10 Gbps | 2.5 / 5 / 10 Gbps
Cable | 1 × STP (shielded) | 2 × UTP (unshielded)
Reach | Up to 15 m | Up to 40 m (target)
Cost | Higher (shielding) | Lower (UTP)
EMC | Better (shielded) | Requires careful routing
Use case | Short backbone links | Longer backbone / trunk
TC14 complements 802.3ch — it is not a competing standard. The two address different link segments within the vehicle: 802.3ch for short, high-density backbone connections (e.g., HPC to switch), and TC14 for longer trunk cables (e.g., front zone controller to rear zone controller).
Notes: TC14 is a newer and still-evolving OPEN Alliance activity. The fundamental trade-off is: single-pair STP (802.3ch) gives you multi-gigabit in a compact cable but is limited to ~15 m and requires shielding, which adds cost and weight. Two-pair UTP (TC14 scope) doubles the copper but eliminates the shield and extends reach to ~40 m, which is needed for trunk cables running the length of a vehicle (e.g., from a front zone controller to a rear zone controller in a zonal architecture — that's easily 4-5 metres in a compact car, 8+ metres in an SUV). The two specifications will coexist: 802.3ch for short, high-density connections (HPC to switch ASIC), TC14 for longer inter-zone trunks.

## Slide 19
Standards ecosystem: how it fits together
IEEE 802
Defines the standard
802.3bw (100BASE-T1)
802.3bp (1000BASE-T1)
802.3ch (MultiGig-T1)
802.3cg (10BASE-T1S)
802.1Q (VLAN)
802.1AS (gPTP)
802.1Qbv (TAS)
OPEN Alliance SIG
Drives adoption
TC1/TC9/TC12 — compliance
TC10 — sleep/wake
TC14 — two-pair Ethernet
TC2 — connectors
TC6 — 10BASE-T1S profile
TC8 — EMC testing
Interoperability plugfests
OEM / Tier-1
Deploys in vehicles
System architecture
ECU integration
AUTOSAR stack config
Network design (VLAN, QoS)
Wiring harness design
End-of-line testing
Vehicle validation
Notes: This slide shows how the three pillars work together: IEEE creates the formal standards (PHY electrical specifications, MAC protocol, TSN mechanisms). OPEN Alliance SIG takes those standards and creates the automotive ecosystem around them: compliance test specs so vendors can verify interoperability, application-level specs like TC10 sleep/wake that IEEE doesn't define, connector and cabling specs, and plugfest events where vendors verify that their PHYs actually work together. OEMs and Tier-1s then take the complete package and deploy it into vehicles, configuring AUTOSAR stacks, designing VLANs and QoS policies, and validating the system end-to-end.

## Slide 20
Summary — key takeaways
Domain → Zonal
Vehicle E/E architecture is transitioning from functional domain grouping to location-based zonal grouping, driven by wiring cost reduction and SDV enablement. Ethernet is the backbone technology.
OSI model
IEEE 802 covers Layers 1–2 (PHY + MAC). Automotive adds TSN at L2 (802.1AS, 802.1Qbv) and SOME/IP at L5–7 for service-oriented communication.
IEEE 802 family
Key automotive PHY standards: 802.3bw (100M), 802.3bp (1G), 802.3ch (multi-gig) — all single twisted pair. 802.1Q/AS/Qbv provide VLAN, time sync, and traffic shaping.
OPEN Alliance SIG
Bridges the gap between IEEE standards and vehicle deployment. TC10 solves Ethernet sleep/wake for energy management. TC14 enables multi-gig over two-pair UTP for longer reach.

## Slide 21
Further reading & Q/A
References
IEEE 802.3 — ieee802.org/3
IEEE 802.1 TSN Task Group — ieee802.org/1/pages/tsn.html
OPEN Alliance SIG — opensig.org
OPEN Alliance TC10 Sleep/Wake specification v2.x
AUTOSAR Adaptive Platform — autosar.org
SOME/IP Protocol Specification — autosar.org/standards
Questions?