## Slide 1
Ethernet Frame Formats,
EtherType & Frame Filtering
Ethernet II · VLAN tagging · EtherType registry · Layer 2 forwarding · Automotive context

## Slide 2
Agenda
1
Frame Anatomy
Dst MAC, Src MAC, EtherType/Length, Payload, FCS
2
Ethernet II vs 802.3/LLC
EtherType-based vs length-based — which dominates and why
3
VLAN Tagging
C-TAG (0x8100), S-TAG (0x88A8), PCP, Q-in-Q double tagging
4
EtherType Registry
Key EtherType values: IPv4, IPv6, ARP, PTP, MACsec, AVTP
5
Frame Filtering
MAC learning, FDB lookup, VLAN-based forwarding decisions
6
Automotive Context
Latency, filtering contracts, jumbo frames, multicast risk

## Slide 3
1
Ethernet Frame Anatomy
The Layer 2 envelope: addressing, type/length, payload, integrity check

## Slide 4
Ethernet Frame — Fields On The Wire
Preamble+SFD
8 B
Dst MAC
6 B
Src MAC
6 B
EtherType
or Length
2 B
Payload (data)
46–1500 B
Pad
0–46 B
FCS
4 B
Preamble+SFD: PHY-level only, not visible to MAC
≥ 0x0600 → Ethernet II (protocol ID)
≤ 1500 → IEEE 802.3 (byte count)
CRC-32 over entire frame
Field
Size
Purpose
Destination MAC
6 bytes
Unicast, multicast, or broadcast (FF:FF:FF:FF:FF:FF)
Source MAC
6 bytes
Always unicast — identifies the transmitting station
EtherType / Length
2 bytes
≥ 0x0600: protocol ID (Ethernet II). ≤ 1500: payload byte count (IEEE 802.3)
Payload
46–1500 B
Upper-layer data; padded to 46 B minimum to meet 64-byte minimum frame size
FCS
4 bytes
CRC-32 integrity check — receiver discards frame on mismatch

## Slide 5
2
Ethernet II vs 802.3/LLC
Two interpretations of the same 2-byte field after the source MAC address

## Slide 6
Ethernet II vs IEEE 802.3+LLC — Frame Layout
Ethernet II (dominant modern format)
Dst MAC
6B
Src MAC
6B
EtherType
2B
Payload
46–1500B
FCS
4B
EtherType ≥ 0x0600 → directly names the payload protocol (e.g. 0x0800=IPv4, 0x88F7=PTP)
IEEE 802.3 + LLC/SNAP (legacy)
Dst MAC
6B
Src MAC
6B
Length
2B
DSAP
SSAP
2B
Ctrl
1B
SNAP OUI+Type
5B
Payload
data
FCS
4B
Length ≤ 1500 → protocol identified inside payload via LLC/SNAP, not at Layer 2
Ethernet II
802.3 + LLC/SNAP
2-byte field after Src MAC
EtherType — protocol ID
Length — byte count of data
Protocol identification
Direct at Layer 2
Inside payload via LLC/SNAP
Modern IP / TSN / gPTP
✓ All modern stacks use Ethernet II
✗ Rarely used in modern networking
Automotive backbone
✓ Default for all vehicle protocols
Historical/legacy only

## Slide 7
3
VLAN Tagging
C-TAG (0x8100), S-TAG (0x88A8), PCP priority field, Q-in-Q double tagging

## Slide 8
VLAN Tag Anatomy — The Extra 4 Bytes Inserted After Src MAC
Untagged
Dst MAC
6B
Src MAC
6B
EtherType
2B
Payload
...
FCS
4B
Single-tagged C-TAG (0x8100) — +4 bytes
Dst MAC
6B
Src MAC
6B
TPID
0x8100
2B
TCI
PCP+DEI+VID
2B
EtherType
2B
Payload
...
FCS
4B
TCI = Tag Control Info: PCP (3 bits, priority 0–7) | DEI (1 bit, drop eligible) | VID (12 bits, VLAN 1–4094)
PCP
3 bits
DEI
1 bit
VID
12 bits
Double-tagged Q-in-Q: outer S-TAG (0x88A8) + inner C-TAG (0x8100) — +8 bytes total
Dst MAC
6B
Src MAC
6B
0x88A8
S-TAG
2B
TCI
Outer
2B
0x8100
C-TAG
2B
TCI
Inner
2B
EtherType
2B
Payload
...
FCS
4B
Outer S-TAG 0x88A8 = service/provider domain | Inner C-TAG 0x8100 = customer/endpoint domain

## Slide 9
PCP Values — 802.1p Priority Mapping & Automotive Traffic Classes
Priority Code Point (PCP) — 3 bits in the TCI field, values 0–7:
PCP 7
Network critical
Protocol control: gPTP, STP, reserved
PCP 6
Voice / urgent real-time
Highest-priority application traffic
PCP 5
Video / ADAS streams
Camera feeds, radar, LiDAR — time-sensitive data
PCP 4
Controlled load
Professional AV, controlled-latency services
PCP 3
Excellent effort
Important non-real-time control messages
PCP 2
Reserved
Often treated as best-effort by implementations
PCP 1
Background
Lower than best effort — bulk background transfers
PCP 0
Best effort
Default — no priority assigned to the frame

## Slide 10
4
EtherType Registry
The Layer 2 protocol selector — key values from the IANA/IEEE-802 registry

## Slide 11
Key EtherType Values — IANA / IEEE Registry
EtherType
Protocol
Description
Cat.
0x0800
IPv4
Internet Protocol version 4
IP
0x0806
ARP
Address Resolution Protocol
IP
0x86DD
IPv6
Internet Protocol version 6
IP
0x8035
RARP
Reverse ARP (legacy)
IP
0x8100
C-TAG (VLAN)
Customer VLAN Tag — triggers VLAN processing
VLAN
0x88A8
S-TAG (Q-in-Q)
Service VLAN Tag — outer tag in double-tagging
VLAN
0x88CC
LLDP
Link Layer Discovery Protocol
Mgmt
0x88E5
MACsec
Media Access Control Security (IEEE 802.1AE)
Sec
0x88F7
PTP / gPTP
Precision Time Protocol (IEEE 1588 / 802.1AS)
TSN
0x22F0
AVTP
Audio Video Transport Protocol (IEEE 1722)
TSN
0x8808
Flow Ctrl
Ethernet flow control — PAUSE frames
Mgmt
0x893A
IEEE 1905
Hybrid networking (informational)
Mgmt

## Slide 12
5
Frame Filtering & Forwarding
MAC learning, FDB lookup, VLAN membership checks, flooding decisions

## Slide 13
Bridge Forwarding Logic — Step-by-Step Decision Flow
Frame arrives
on ingress port
Learn source MAC
+VLAN → FDB
VLAN check
Port member
of this VLAN?
No→Drop
DISCARD
Lookup Dst MAC
in FDB
(MAC + VLAN)
Hit →
Known unicast
Forward to
specific port
Egress VLAN filter
Remove non-member
ports
✓ Transmit on approved port(s)
Miss ↓
Unknown UC / MC / BC
Flood within
VLAN domain
⇒

## Slide 14
Unicast, Multicast, Broadcast — Layer 2 Delivery Patterns
→ 1
Unicast
Destination
Specific 6-byte MAC address
Forwarding
Known: forward to one specific port
Unknown: flood within VLAN (FDB miss)
Automotive use
IP traffic, control messages
Risk
FDB miss causes flooding — scale carefully
→ N
Multicast
Destination
01:xx:xx:xx:xx:xx
(LSB of 1st byte = 1)
Forwarding
Flood to all VLAN ports (no IGMP)
Selective if multicast DB exists
Automotive use
gPTP: 01:80:C2:00:00:0E
LLDP, AVTP, SOME/IP multicast
Risk
Flooding if multicast filter not configured — latency risk in vehicles
→ ∞
Broadcast
Destination
FF:FF:FF:FF:FF:FF
(all ones)
Forwarding
Replicate to ALL ports in the
broadcast domain / VLAN
Automotive use
ARP requests, DHCP discover
Risk
Storm risk — must be tightly controlled in automotive backbones
Automotive: broadcast and unknown-unicast flooding is dangerous in vehicle backbones with 100 µs latency budgets. Tight VLAN design and multicast filtering are mandatory engineering requirements.

## Slide 15
6
Automotive Context
Latency, filtering contracts, jumbo frames — vehicle engineering requirements

## Slide 16
Ethernet Frame as a System Contract in Automotive Networks
ETH II
Ethernet II Framing
All modern vehicle protocols — IP, ARP, gPTP, LLDP, MACsec, AVTP — use Ethernet II EtherType framing. EtherType directly identifies every payload at Layer 2.
VLAN
VLAN Tags Are Mandatory Engineering
PCP (3-bit priority) and VID (12-bit domain) are part of the forwarding contract. TSN and AVB use these to segregate traffic. Switches must honour them exactly.
BC/MC
Flood Control Is Safety-Critical
Latency target ~100 µs leaves no room for uncontrolled flooding. Unknown unicast, multicast without state, and broadcast all cause wider replication than intended.
TEST
Filtering Is Actively Tested
OPEN Alliance Layer 2 test specs verify frames go to exactly the expected ports and not to others. Single- and double-tagged frame correctness is proven, not assumed.

## Slide 17
Jumbo Frames — Efficiency vs Serialisation Latency
Jumbo Frames — What They Are
Standard Ethernet payload: 1500 bytes max (IEEE 802.3)
Jumbo frame: payload > 1500 bytes
Common practical limit: ~9000 bytes
Not formally standardised — vendor/system agreement
Benefit: fewer frames for bulk data → lower per-frame overhead → higher throughput efficiency
Automotive Latency Problem
Serialisation delay = time to push all bits onto the link
At 1 Gbit/s: 9000-byte jumbo ≈ 72 µs serialisation time
At 1 Gbit/s: 1500-byte standard ≈ 12 µs serialisation time
Automotive latency target: ~100 µs end-to-end
A single jumbo can consume 72% of total latency budget just on the first hop
Serialisation time at 1 Gbit/s:
1500 B (~12 µs)
12 µs
9000 B (~72 µs)
72 µs
← 100 µs automotive latency budget →

## Slide 18
✓
Key Takeaways
Ethernet frame formats, EtherType, and filtering — the complete picture

## Slide 19
Summary — Ethernet Frames in Automotive Networks
Ethernet II
Dominant format. EtherType field directly identifies payload protocol. All vehicle protocols (IP, gPTP, LLDP, MACsec, AVTP) use Ethernet II.
VLAN Tags (C-TAG/S-TAG)
C-TAG (0x8100) adds PCP (priority 0–7) and VID (VLAN domain 1–4094). In automotive they define the forwarding contract — mandatory, not optional.
EtherType Registry
0x0800=IPv4, 0x88F7=PTP, 0x88E5=MACsec, 0x8100=VLAN, 0x22F0=AVTP. Values ≥ 0x0600 = protocol ID. Values ≤ 1500 = length (802.3 format).
Bridge Filtering
Learn from source MAC. Forward on destination MAC + VLAN (FDB). FDB miss → flood. Egress VLAN filter removes non-member ports before transmit.
Broadcast / Multicast
Broadcast = FF:FF:FF:FF:FF:FF, flooded everywhere. Uncontrolled flooding is dangerous in vehicles with tight latency budgets. Must be engineered.
Jumbo Frames
Payloads > 1500 B. 9000-byte frame = 72 µs serialisation at 1 Gbit/s — 72% of a 100 µs automotive budget. Use only for non-time-critical bulk traffic.

## Slide 20
Thank You
Ethernet II · VLAN C-TAG / S-TAG · EtherType Registry · Layer 2 Filtering · Automotive Frame Engineering