## Slide 1
10BASE-T1S
Physical Layer Collision Avoidance, OPEN Alliance TC14,
and TC10 Sleep/Wake
A Technical Deep Dive for Automotive Ethernet Edge Networks

## Slide 2
01
The Problem at the Vehicle Edge
Why CAN and LIN are no longer enough
2

## Slide 3
Devices at the Vehicle Edge
These devices do not need 100 Mbps or 1 Gbps.
They need modest bandwidth, low wiring cost, and simple integration.
Door Module
Seat Controller
Lighting Controller
Sensor Cluster
Local Actuator
Historically served by CAN and LIN
10BASE-T1S brings Ethernet framing and tooling into this low-cost domain
without forcing every node onto a switched point-to-point link.
3

## Slide 4
10BASE-T1S is not 'cheap Ethernet'
It is Ethernet redesigned for a very specific physical situation:
A short-reach, single twisted-pair segment
where multiple nodes share the same medium
That shared-medium part is why you cannot understand 10BASE-T1S
without understanding what happens when multiple nodes want to talk.
4

## Slide 5
02
Two Worlds Under One Name
Point-to-point vs. multidrop operation
5

## Slide 6
Point-to-Point vs. Multidrop
POINT-TO-POINT
Node A
Node B
Full-duplex or half-duplex
Two nodes, one pair
MULTIDROP
N0
N1
N2
N3
N4
Half-duplex only
8+ inline PHYs, 25 m topology
The interesting engineering starts with multidrop.
A shared medium immediately raises one question:
If two nodes want to transmit at nearly the same time, who gets the cable first?
6

## Slide 7
Why a Shared Medium Is Hard
SWITCHED NETWORK
Every link gets its own
collision-free point-to-point channel
No collisions by design
vs
MULTIDROP BUS
If two nodes launch energy
at the wrong time, waveforms interfere
Collision
CSMA/CD: Listen → Transmit → Detect collision → Back off → Retry
This works, but access time is no longer bounded by a fixed schedule.
Collisions and random backoff stretch latency and create unfairness.
7

## Slide 8
03
Clause 147 and Clause 148
The PHY foundation and the arbitration discipline
8

## Slide 9
Clause 147: What Happens on the Wire
Differential Manchester Encoding
Two-level DME at 12.5 megabaud
Self-clocking: timing embedded in transitions
Intrinsically balanced signal
Robust clock and data recovery in noisy environments
4B/5B Coding in PCS
Improved EMC performance
Supports out-of-band signalling
Not raw unsupervised logic bits
Built for harsh automotive cable
Clause 147 mentions optional PLCA support,
but Clause 147 alone does not give collision-free multidrop behaviour.
9

## Slide 10
The Foundational Split
Clause 147
The shared Ethernet
physical layer
Clause 148
The disciplined way to use
that shared medium
PLCA is optional. It improves throughput, fairness, and latency.
It works with CSMA/CD — it does not replace Ethernet.
10

## Slide 11
What PLCA Really Does
PLCA controls permission to start transmitting.
It does not change the frame format. The frames are still Ethernet frames.
WITHOUT PLCA
All nodes may try at once.
Collisions resolved after the fact.
Random backoff stretches latency.
WITH PLCA
Only one node has the right
to start at a given moment.
No physical collisions on the line.
11

## Slide 12
The PLCA Cycle
BEACON
(Node 0)
TO 0
Send
TO 1
Idle
TO 2
Idle
TO 3
Send
TO ...
TO N
Idle
One PLCA cycle = 1 Beacon + (N+1) Transmit Opportunities
Active node
Node 3 has data. It waits through TO 0-2, then transmits during TO 3.
COMMIT
If MAC needs time before data appears, PHY sends COMMIT to hold the turn.
Idle node
Has nothing to send. Opportunity timer expires quickly. Cycle moves on.
12

## Slide 13
PLCA Is Not TDMA
TDMA
Slot 0
DATA
Slot 1
EMPTY
Slot 2
EMPTY
Slot 3
DATA
Slot 4
EMPTY
Fixed slots reserved whether data exists or not → bandwidth wasted
PLCA
TO 0
DATA
TO 1
TO 2
TO 3
DATA
TO 4
Only right-to-start is reserved. Idle turns yield quickly → bandwidth preserved
Edge networks are bursty. PLCA gives a cheaper compromise
between totally random access and hard scheduled bus.
13

## Slide 14
04
Configuration Parameters
The knobs engineers actually set in a real device
14

## Slide 15
Node Identity and Count
ID — Node Identifier
Must be unique across the multidrop segment for collision-free operation.
ID = 0
Coordinator
ID = 255
PLCA suspended
Failure modes: duplicate IDs, or nodes accidentally left at 255.
NCNT — Node Count
Set on the coordinator. Must cover the maximum installed population.
Determines how many transmit opportunities exist per cycle.
Directly affects worst-case access latency.
Set too low → some nodes never get a turn.
15

## Slide 16
Timing and Burst Configuration
TOT — Transmit Opportunity Timer
Default: 32 bit-times
Must be set equally across all nodes for collision-free operation.
Default guarantees proper operation over a 25 m twisted-pair inline topology.
MAXBC — Burst Count
How many additional packets a node may send during its own TO.
Set to 0 = burst mode off.
BTMR — Burst Timer
Wait time for MAC to deliver the next packet before yielding.
Must exceed MAC IPG + added TX latency.
Tradeoff: more burst capability improves efficiency for a busy producer, but lengthens the wait for other nodes.
16

## Slide 17
Diagnostic Bits
Real bring-up failure signatures, not theoretical edge cases.
RXINTO
Received a packet during own transmit opportunity
Root cause: Duplicate node ID on the segment
UNEXPB
Unexpected beacon detected on the coordinator
Root cause: More than one coordinator
BCNBFTO
Beacon arrived before this node received its turn
Root cause: NCNT misconfiguration on coordinator
17

## Slide 18
05
OPEN Alliance TC14
Turning the IEEE foundation into an automotive ecosystem
18

## Slide 19
What TC14 Adds Beyond the IEEE Clauses
IEEE tells you how the PHY works. It does not tell you how to build,
debug, sleep, wake, and interop-test an automotive controller-transceiver combination.
Conformance and interoperability test specifications
Advanced diagnostic features
System implementation specification
PMD transceiver interface definition
PLCA management registers
Topology discovery
Sleep/wake collaboration
"TC14 v1.5" is not one PDF. TC14 is a family of specs. Version 1.5 applies to
the PMD interface and interop test suite. Other TC14 docs have different versions.
19

## Slide 20
The PMD Transceiver Interface (v1.5)
What v1.5 added: topology discovery, RX-pin RZI encoding,
Energy Detect pin filtering, and wake/sleep support.
HOST
CONTROLLER
10BASE-T1S
TRANSCEIVER
RX pin (data)
Energy Detect
MDC / MDIO
(config mode)
Same physical pins serve dual roles: data mode vs. configuration mode.
20

## Slide 21
The Right Mental Model
OPEN Alliance TC14
Automotive Integration Ecosystem
IEEE Clause 148 — PLCA
Arbitration Discipline
IEEE Clause 147 — 10BASE-T1S PHY
Shared-Medium Ethernet Foundation
▲
▲
21

## Slide 22
06
TC10 Sleep/Wake
Why automotive Ethernet needed its own power-state protocol
22

## Slide 23
Sleep/Wake Is Not Just "Power Down the PHY"
It must be a coordinated signalling system that avoids false wake-ups,
supports partial networking, and works across PHYs and switches.
CSMA/CD MAC compliance
MII-family compliance
Global network wake-up < 250 ms
Wake-up fully at physical layer level
Controlled selective shutdown
AUTOSAR network management compliance
No unwanted wake-ups from noise
23

## Slide 24
Classic TC10: Three Commands
The point-to-point sleep/wake handshake model.
LPS
Low Power Sleep
Requests sleep. Both partners must exchange LPS for the handshake to complete.
WUR
Wake-Up Request
Propagates a wake request over an active link between two partners.
WUP
Wake-Up Pulse
Wakes a passive or sleeping link. The electrical signal that rouses a dormant PHY.
If the handshake fails, the PHY returns to normal operation — never leaves the link half-dead.
24

## Slide 25
10BASE-T1S Sleep/Wake Is Different
A 10BASE-T1S segment is not a simple point-to-point link.
P2P TC10 Problem
How do two ends of one link
sleep and wake correctly?
10BASE-T1S Problem
How do many nodes on one shared
segment sleep and wake without
corrupting traffic or confusing each other?
The 10BASE-T1S spec adds:
A dedicated Power Management Client model
One segment wake-up command: Wake-Up Pulse (WUP)
A new set of service primitives for shared-segment operation
25

## Slide 26
Service Primitives: Local Control
Control and report the state of the local PHY only.
LowPowerEntryLocal.request
"Put my local PHY into low power."
Shuts down the local PHY in a controlled way without corrupting ongoing
transmissions on the link segment. This is not "turn the whole network off."
WakeupLocal.request
"Wake my local PHY back up from low power."
Purely local wake request. Triggered by ECU logic, ignition, or a local wake pin.
Transitions only the local PHY out of low power.
26

## Slide 27
Service Primitives: Segment Wake
Wakeup.request
"Send a wake-up onto the segment so all supported nodes can wake."
Requests a Wake-Up Pulse be communicated to all nodes on the segment.
If the device is itself in low power, this implicitly means WakeupLocal first, then Wakeup.request.
Wakeup.indication
"A wake-up event has been detected."
Covers both a WUP detected on the segment and one from a local wake pin.
Reports that wake-up happened regardless of whether the source was local or from the wire.
27

## Slide 28
Wake Forwarding in a Multiport Switch
Branch A
(wake source)
WakeupFwd
.indication
ZONAL SWITCH
Power Management Logic
WakeupFwd
.request
Branch B
WakeupFwd
.request
Branch C
WakeupForward.indication = wake event arrived here, to be relayed
WakeupForward.request = propagate that wake event out on this port
28

## Slide 29
The Wake-Up Pulse Pattern
A structured signal: electrically distinctive yet short enough not to damage bus efficiency.
SUSPEND
6 DME T symbols
Wake-Up
Tone
12 periods
625 kHz
COMMIT
24-26 DME
J symbols
ESD /
ESDOK
32.0 — 32.8 µs total (32.4 µs typical)
Other nodes on the segment must not start normal transmissions
while a Wake-Up Pulse is active.
29

## Slide 30
Quiet Segment vs. Partial Segment
QUIET
No physical-medium activity.
No beacons, no frames, nothing on the wire.
PARTIAL
At least one node transmitting, including
PLCA beacons. Even beacons-only ≠ quiet.
Wake-up timing on a partial segment:
TWU_Start_partial < TWU_Start_quiet(max) + maxPLCACycleTime
On an active segment, wake-up latency is also an arbitration problem.
The wake request must respect the transmit-opportunity structure.
30

## Slide 31
PLCA Pause During Wake-Up
This detail separates "I know the acronym" from "I understand the system."
The paused variable suspends transmit-opportunity generation
and stops the Reconciliation Sublayer from conveying data to the PHY.
resume_timer = 240 ± 5 bit-times after wake-up reporting ends.
Without pause
Normal TO generation could interfere with wake signalling on an active shared segment.
With pause
Wake activity temporarily takes control of the medium. Normal PLCA resumes only after wake is handled.
31

## Slide 32
07
Bring-Up Realities
What a real engineer has to get right
32

## Slide 33
The Bring-Up Checklist
One node configured as coordinator (ID = 0)
Every other node has a unique identifier
Coordinator NCNT covers the largest installed population
Transmit Opportunity Timer matches across all nodes
Burst mode disabled or deliberately engineered for traffic pattern
Wake behaviour verified on both quiet and partial segments
PMD interface: host-transceiver agreement on command timing,
RX-pin interpretation, Energy Detect, reset sequencing, wake handshakes
33

## Slide 34
Failure Signatures to Watch For
These look "Ethernet-like" at first, but the root cause is shared-medium orchestration.
Random corruption on the bus
Duplicate node identifiers
Missing access opportunities
Wrong node count (NCNT too low)
Unstable bus behaviour
Mismatched transmit-opportunity timing
Some nodes seem dead,
others appear fine
Incorrect wake sequencing
The OPEN Alliance diagnostic bits exist precisely because these are real field problems.
34

## Slide 35
10BASE-T1S Is a Complete Edge-Networking Concept
TC10 Sleep/Wake
Coordinated power-state discipline
OPEN Alliance TC14
Automotive productization ecosystem
Clause 148 — PLCA
Collision-free arbitration discipline
Clause 147 — 10BASE-T1S PHY
Shared-medium Ethernet foundation
35