## Slide 1
ETHERNET TRAFFIC MANAGEMENT
Frame Preemption, PAUSE Frames
& Link Aggregation
IEEE 802.1Qbu · IEEE 802.3br · IEEE 802.3x · IEEE 802.1AX

## Slide 2
What happens when Ethernet traffic
competes for the same resource?
Serialization delay · Buffer overload · Bandwidth limits
Three bottlenecks. Three distinct solutions.

## Slide 3
Three Bottlenecks. Three Solutions.
Frame Preemption
PROBLEM
Latency from serialization
SOLUTION
Express MAC interrupts preemptable traffic mid-frame
PAUSE Frames
PROBLEM
Short-term link overload
SOLUTION
Receiver asks sender to stop non-control traffic briefly
Link Aggregation
PROBLEM
Capacity & resilience
SOLUTION
Multiple physical links behave as one logical link

## Slide 4
SECTION
Part 1: Frame Preemption
IEEE 802.1Qbu & IEEE 802.3br

## Slide 5
The Serialization Problem
Ethernet sends bits serially. Once a frame begins transmission, the link is busy until that frame is done.
If a time-critical frame arrives just after a large low-priority frame has started — the urgent frame must wait.
⚠ The problem is worst at lower link speeds (100Mbps), where serialization delay is proportionally larger.
Large Low-Priority Frame (in progress)
URGENT
WAITING
...still waiting...
← Without preemption: urgent frame is blocked →
TIME →

## Slide 6
Two Standards. One Solution.
IEEE 802.1Qbu
The Bridge Side
Forwarding enhancements
Defines which traffic classes are treated as express vs preemptable
Operates at the bridged LAN level
works with
IEEE 802.3br
The Ethernet Port Side
MAC Merge sublayer
Physically interrupts and resumes preemptable transmissions
Operates at the Ethernet port level

## Slide 7
A Two-Class Model: Express vs Preemptable
Frame preemption is not 'any priority can cut in anywhere.' It creates one strict boundary:
Express MAC (eMAC)
Handles urgent, latency-sensitive traffic
Can interrupt a preemptable transmission
Wins arbitration when both sides are ready
VS
Preemptable MAC (pMAC)
Handles best-effort, non-critical traffic
May be interrupted mid-frame
Fragmented and resumed after express traffic passes

## Slide 8
The MAC Merge Sublayer
The key invention of 802.3br — a new arbitration and fragmentation engine:
Higher-Layer Traffic
Traffic Class Decision
Express MAC
(eMAC)
Preemptable MAC
(pMAC)
MAC Merge Sublayer
Physical Layer
Arbitrates between eMAC and pMAC transmit queues
Handles receive-side reassembly and fragment checking
Verifies link partner supports preemption before activating
A new sublayer — not just a scheduler reorder trick

## Slide 9
What Actually Happens During Preemption
The preemptable frame is NOT discarded — it is split and resumed.
1
Preemptable frame starts transmitting
2
Express frame arrives
3
MAC Merge waits for a legal cut point
4
Preemptable frame is suspended (partial fragment sent)
5
Express frame is transmitted fully
6
Remaining preemptable fragments sent as continuations
Fragment types — mPacket markers: SMD-E (express) · SMD-S0..S3 (preemptable start) · SMD-C0..C3 (continuation)

## Slide 10
Preemption Is Controlled, Not Instantaneous
A preemptable frame cannot be chopped at any random bit boundary.
60
Minimum 60 octets transmitted
Preemption only occurs after at least 60 octets of the preemptable frame have been sent.
64
Minimum 64 octets remaining
At least 64 octets (including FCS) must still remain to be transmitted.
⊕
addFragSize controls the earliest cut point
Cut point = 64 × (1 + addFragSize) – 4 octets sent. Non-final fragments must meet the minimum size.
✓
Continuation fragments are numbered
A modulo-4 fragment count lets the receiver detect loss or mis-ordering during reassembly.

## Slide 11
Hold & Release: The Scheduler's Hook
The MAC Merge sublayer is controlled via two simple primitives — giving TSN schedulers precise timing control.
HOLD
Causes the MAC Merge sublayer to stop transmitting preemptable traffic.
Used when an express transmission window is imminent — prevents new preemptable frames from starting.
RELEASE
Allows preemptable traffic to resume transmission.
Bound: response within (1240 + 512 × addFragSize) bit times after the Hold request.
Preemption helps in two ways: interrupting in-progress frames AND preventing new preemptable frames from starting.

## Slide 12
Verification: Preemption Doesn't Activate Blindly
Two ports must confirm they both support frame preemption before it becomes active.
Port A sends
SMD-V Verification Packet
Port B replies with
SMD-R Response Packet
Valid response received
→ Preemption Activated
Why this matters:
If one side fragments preemptable traffic but the far end doesn't understand fragment markers, the link would fail silently.
Verification can be disabled in engineered closed networks — but that's a deliberate engineering choice, not the default.

## Slide 13
What Preemption Fixes — and What It Doesn't
✓ Good At
Reducing serialization delay from large low-priority frames
Preventing urgent frames from waiting behind bulky best-effort traffic
Especially impactful at lower link speeds (100Mbps)
✗ Not a Cure-All
Does not replace scheduling, bandwidth reservation, or queue design
Only helps the first conflicting urgent frame — when many urgent frames compete, scheduling is still needed
Does not guarantee near-zero jitter alone

## Slide 14
SECTION
Part 2: PAUSE Frames
IEEE 802.3x Flow Control

## Slide 15
PAUSE Frames: A Different Problem Entirely
PAUSE frames don't reduce serialization latency. They solve a completely different problem:
"One endpoint on a full-duplex link is temporarily congested — let it ask its neighbor to stop sending non-control frames for a short interval."
Congestion reaction tool, not a real-time scheduling tool
Link-local only — not end-to-end flow control
Only makes sense for transient overload on one full-duplex hop
IEEE 802.3x is explicit: not intended as a steady-state congestion solution

## Slide 16
Where PAUSE Lives in the Stack
PAUSE is not just another Ethernet payload — it lives in a special MAC Control sublayer:
Normal MAC Client (LLC / Bridge Relay Entity)
MAC Control Sublayer ← PAUSE lives here
Media Access Control (MAC)
Physical Layer
Inserted by 802.3x between normal MAC and its client
Controls link behavior directly — not a transport-layer or app function
This is why PAUSE is blunt: it acts on the whole transmitter, not on a specific flow

## Slide 17
PAUSE Frame Format
Destination Address
01-80-C2-00-00-01
Well-known multicast address
EtherType
0x8808
MAC Control frames
Opcode
0x0001
PAUSE operation
Pause_time
0 – 65535 slot times
Duration to pause; later frames can override
Padding
(to minimum Ethernet frame length)
Pad to 64 bytes minimum
Effect: the recipient stops transmitting non-control frames for the specified interval. Later PAUSE frames override any current pause in progress.

## Slide 18
PAUSE: Useful — But Dangerously Coarse
Why It Helps
Protects a temporarily overloaded receiver or switch from immediate packet drops.
A switch with limited memory can ask its full-duplex neighbor to slow down instead of dropping frames at once.
Why It's Dangerous
Does NOT pause only the "bad flow" — it stops ALL non-control frames
Suppresses OAM messages and other traffic that wasn't causing the problem
Can spread congestion upstream
IEEE itself warned: not a steady-state congestion solution

## Slide 19
Symmetric vs Asymmetric PAUSE
PAUSE use is also a policy decision — the standard defines signaling, not policy.
Symmetric
Either side can throttle the other.
Typically used on switch-to-switch links where both sides may be overwhelmed.
Asymmetric
Only one direction is enabled.
Often used on switch-to-host links — the switch can throttle the host, but the host cannot throttle the switch.
Two devices can both "support PAUSE" and behave very differently operationally.

## Slide 20
SECTION
Part 3: Link Aggregation
IEEE 802.1AX (formerly IEEE 802.3ad)

## Slide 21
When One Link Isn't Enough
Link Aggregation addresses two gaps a single physical link cannot fill:
↑↑
Insufficient Bandwidth
One 1 Gbps link may not carry the required load. Aggregating four links raises available throughput across all conversations.
⟳
Single Point of Failure
One physical link can go down. A LAG can survive member failures and continue serving higher layers with minimal disruption.

## Slide 22
Link Aggregation Group (LAG) Architecture
The higher layer sees one logical link. Underneath, the Aggregator maps onto active physical members.
Higher Layer / Bridge Port
Aggregator (logical link)
AggPort
MAC
AggPort
MAC
AggPort
MAC
Aggregation Ports — typically one per physical MAC
Aggregators — represent the logical bundle to the higher layer
LACP — dynamically attaches/detaches Aggregation Ports
LAG sublayer sits between bridge ports and MAC instances

## Slide 23
LACP: The Control Protocol, Not the Data Plane
LACP decides membership — it does NOT define how packets are striped across links.
Actor & Partner
Each side advertises system IDs, port IDs, and keys. "Actor" = my side. "Partner" = the remote side.
Key Agreement
Ports with matching keys and consistent system view can be selected and attached to the same aggregate.
Selection Logic
LACP evaluates receive, periodic-transmission, selection, and mux state to determine which ports join the LAG.
Dynamic Membership
If one side's view of the bundle changes (e.g., a link fails), LACP ensures the other side knows — preventing silent failures.

## Slide 24
Load Sharing Without Reordering: Conversations
The standard only requires: frames whose relative order must be preserved travel on the same link.
A sequence of frames that must preserve order = a CONVERSATION
Implementations hash header fields (src/dst MAC, VLAN, EtherType, IP src/dst, TCP ports) to select the member link for each conversation
One large flow typically maps to one member — not spread across all links
Four 1 Gbps members ≠ 4 Gbps for a single TCP session
Load sharing quality depends on the distribution algorithm and traffic mix — the standard doesn't mandate the algorithm
Link Aggregation provides aggregate capacity across many conversations — not magic bandwidth multiplication per flow.

## Slide 25
SECTION
Putting It Together
Comparing the three mechanisms

## Slide 26
Three Mechanisms. Three Problems. One Clean Division.
Frame Preemption
Latency Mechanism
Scope: within one port's transmit behavior
Action: interrupts pMAC frames so eMAC frames pass sooner
Selectivity: express vs preemptable only
Standard: 802.1Qbu + 802.3br
PAUSE Frames
Flow-Control Mechanism
Scope: across one full-duplex link
Action: stops ALL non-control frame transmission
Selectivity: none — blunt link-wide stop
Standard: 802.3x MAC Control sublayer
Link Aggregation
Capacity & Resilience
Scope: across multiple physical links
Action: presents several links as one logical link
Selectivity: per-conversation assignment
Standard: 802.1AX (LACP)

## Slide 27
Six Common Misconceptions — Corrected
✗
Any higher-priority frame can cut in anywhere.
✓ Only Express MAC interrupts preemptable MAC. The cut point is also constrained by addFragSize rules.
✗
Preemption eliminates the need for scheduling.
✓ Preemption helps the first conflicting urgent frame. For many competing urgent flows, scheduling is still required.
✗
PAUSE is general end-to-end congestion control.
✓ PAUSE is link-local, transient, and explicitly not an end-to-end or steady-state solution.
✗
PAUSE only slows the 'bad flow.'
✓ PAUSE stops ALL non-control frames — including OAM messages unrelated to the congestion.
✗
4 links in a LAG = 4× bandwidth per flow.
✓ Order-sensitive conversations ride one member. Aggregate capacity grows; single-flow throughput usually doesn't.
✗
802.3ad and 802.1AX are different features.
✓ 802.3ad is the historical origin. 802.1AX is the modern standard family; the 2020 revision maintains full interoperability.

## Slide 28
SUMMARY
Three Tools. Three Problems. One Principle.
Frame Preemption
Large low-priority frames block urgent traffic. The MAC Merge sublayer (802.3br) splits preemptable frames so Express MAC traffic passes first.
PAUSE Frames
Short-term buffer stress on a full-duplex link. MAC Control sublayer (802.3x) tells the neighbor to stop non-control frames temporarily.
Link Aggregation
One link lacks bandwidth or resilience. IEEE 802.1AX + LACP bundle multiple links into one logical path with conversation-based load sharing.
Frame Preemption manages latency · PAUSE manages transient overload · Link Aggregation manages capacity + resilience