## Slide 1
Ethernet Link Health
Energy Efficient Ethernet | Low Power Idle
Layer 1 & 2 Counters | Insertion & Return Loss
How do you know whether an Ethernet link is healthy, efficient, and electrically well-behaved?

## Slide 2
Four Topics. One Connected Story.
Energy Efficient
Ethernet
Manages power
on a healthy link
->
Low Power
Idle
Implements the
power-saving behavior
->
Layer 1 & 2
Counters
Shows where
failures appear
->
Insertion &
Return Loss
Explains why
failures happen
Electrical impairments cause physical errors, which cause frame errors. Power state affects timing.

## Slide 3
The Problem EEE Solves
A conventional Ethernet physical layer burns a large portion of its power budget just staying ready, even when no useful traffic is flowing.
Why not just shut the link off?
The receiver maintains timing recovery, equalization, and link integrity state. A full shutdown causes retraining and looks like a link failure to higher layers.
Power Budget
Always-on PHY readiness
Active data transmission
Management overhead
Most power wasted at 0% load

## Slide 4
EEE Answer: Controlled Low-Power Mode
IEEE 802.3az-2010: transition to lower power without appearing as a link-down event to higher layers
✓ Preserves logical link
Higher-layer protocols see the link as up throughout the entire low-power cycle
✓ Scales with utilization
Power tracks actual traffic load rather than worst-case capacity planning
✓ Standardized behavior
IEEE 802.3az defines the rules so both endpoints interoperate cleanly
✓ Not a crude shutdown
A carefully managed low-power operating mode, not simply turning off the port

## Slide 5
Low Power Idle: The Core Idea
When there is traffic — run normally.
When there is no traffic — enter a controlled low-power mode and wake rapidly when needed.
IEEE: "Transmit data as fast as possible, then return to Low Power Idle"
Traditional Ethernet Idle
· Keeps all circuits active
· Continuous signalling
· Full power at 0% load
· No wake delay
Low Power Idle
· Powers down unused circuits
· Periodic refresh only
· Power scales with load
· Small wake-up cost

## Slide 6
The LPI Timing Vocabulary
To understand LPI behavior you must know these five terms:
Ts — Sleep Time
Duration the PHY sends Sleep symbols before going quiet
Tq — Quiet Duration
Duration the PHY remains quiet before a mandatory refresh
Tr — Refresh Duration
Duration of Refresh symbols sent for timing recovery and coefficient sync
Tw_PHY — PHY Wake Time
Time the physical layer itself needs to resume active state
Tw_Sys — System Wake
Extra wait after PHY wakes before data is sent, lets receiving system become ready

## Slide 7
The LPI State Machine
The transmit side cycles through a managed sequence, not a simple on/off switch:
ACTIVE
Normal traffic
->
SLEEP
Assert LPI intent
->
QUIET
Power saved here
->
REFRESH
Maintain receiver state
->
WAKE
Transition back
->
ACTIVE
Resume traffic
Most energy saved in QUIET
REFRESH prevents receiver loss
WAKE ensures safe resume
Why does REFRESH matter?
Without periodic refresh, the receiver gradually loses timing recovery and adaptive filter state it needs for fast reliable recovery. The quiet wire would slowly become an unusable wire.

## Slide 8
Energy Savings vs. Wake Latency
Energy saving is not free. When a frame arrives during LPI, the transmitter cannot instantly return to active mode.
More Energy Saved
Higher First-Frame Latency
<-->
Longer wake times = better savings but worse first-frame delay
Best fit: Bursty traffic
Idle intervals long enough to amortize the wake cost easily
Poor fit: Constant streams
Little idle time means few savings but still adds engineering complexity
LLDP negotiation
After link establishment, LLDP can negotiate different wake times between partners

## Slide 9
When Should You Use EEE?
Not automatically. It depends on traffic pattern, latency tolerance, wake behavior, and platform implementation.
Good Fit
· Bursty, irregular traffic
· Latency-tolerant applications
· Low-utilization access/edge ports
· Green data center deployments
Use With Care
· Latency-sensitive real-time flows
· Links near saturation (little idle time)
· Platforms with slow wake policy
· Partners with mismatched EEE support
EEE mainly saves physical-layer power. System-level savings depend on how well the platform implements policies around it.

## Slide 10
Shift to Observability: L1 and L2 Counters
Counters tell you where a failure appears, not always why. But knowing where is the essential first step.
Layer 1 Counters
-> Is the physical link healthy?
· Is the link up or flapping?
· Is the receiver seeing clean signalling?
· Are symbols or coding blocks being lost?
· Is the problem electrical or transceiver-related?
Layer 2 Counters
-> Are Ethernet frames arriving intact?
· Are valid frames being received?
· Are Frame Check Sequences failing?
· Are frame sizes malformed?
· Are PAUSE frames being exchanged?
Electrical problems usually start as Layer 1 trouble and later manifest as Layer 2 damage.

## Slide 11
Layer 1 Counters: Measuring Signalling Health
"The link is up" is a very weak health test.
A link can be up while the physical receiver fights errors continuously. Some are corrected, some discarded before a valid frame forms, some propagate upward as broken frames. Layer 1 counters catch degradation early.
-> Link up / down transition count
-> Carrier-loss conditions
-> Physical receive errors
-> Symbol or code-group errors
-> Synchronization loss events
-> PHY coding sublayer error counts
Why L1 counters matter more than you think:
A link at barely acceptable margin may show zero Layer 2 errors for hours while Layer 1 counters quietly climb. Catching that early is the difference between planned maintenance and an unexpected outage.

## Slide 12
Layer 2 Counters: What Each One Tells You
FCS / CRC Errors
Valid-size frames with a failed integrity check. Points to corruption in transit: physical issues or duplex mismatch.
Alignment / Frame Errors
CRC error plus non-integer octet count. Receiver failed to reconstruct a clean frame boundary, usually physical trouble.
Runts and Giants
Frames outside size limits. Giants exceed max IEEE 802.3 size with bad FCS: corrupt transmission or severe payload distortion.
PAUSE / Flow Control
One side is requesting silence. Not a fault by itself, but a strong signal of buffer pressure or pipeline stress downstream.
Summary Input Errors
Aggregates multiple specific categories. Not a clean arithmetic sum of visible counters, so read it carefully.

## Slide 13
The Chain: L1 Problems Become L2 Damage
Physical layer impairments do not stay contained. They propagate upward through a predictable sequence:
Electrical
Impairment
High insertion loss
Poor return loss
->
PHY Decoding
Stress
Reduced eye
Equalization strain
->
Symbol /
Carrier Errors
L1 counters
begin climbing
->
Bad FCS /
Malformed Frame
L2 counters
now increasing
->
Packet Loss
or Retries
Application sees
performance issues
Why this chain matters for troubleshooting:
If you see rising FCS errors but have no concept of return loss or insertion loss, you are treating symptoms without understanding cause. The counters are downstream effects of physics happening at the signal level.

## Slide 14
Insertion Loss: Forward Attenuation
How much signal power is lost as it travels from transmitter to receiver?
TX
Cable
Connector
PCB via
Magnetics
RX
(weaker)
Signal attenuated across the full path ->
Low = Better
Less signal is lost along the path; receiver gets more margin
Length Matters
More conductor length, more attenuation along the way
Freq. Matters
Standards note: impairments increase with frequency

## Slide 15
Return Loss: Reflections from Mismatch
How much of the transmitted signal bounces back because the channel impedance is not uniform?
TX
-> Incident signal
MISMATCH
<- Reflected signal (bounces back)
-> (reduced)
RX
High = Better
Less reflected signal means more of the incident wave continues forward cleanly
Reflections distort
Alter zero crossings and reduce receiver margin on fast differential links
Sources: connectors
Vias, traces, magnetics, any impedance discontinuity is a potential reflector

## Slide 16
Two Different Problems, Both Required
Insertion Loss
Forward-path attenuation.
Signal weakens as it travels.
Lower values are worse.
not equal
Return Loss
Backward reflection from mismatch.
Signal bounces from discontinuities.
Higher values are better.
They interact and can mask each other
Acceptable insertion loss + poor return loss: channel passes OK signal but one connector is badly mismatched. Very high insertion loss + masked reflections: heavy attenuation reduces visible reflection at far end, but both problems are real. Conclusion: A channel can fail from too little signal, too much reflection, or both at once.

## Slide 17
Troubleshooting: Putting It All Together
When a port behaves badly, start by asking: is the problem power-state behavior, physical signalling quality, or frame integrity?
1
Wake or Latency Symptom?
Check EEE and LPI. Is wake policy too aggressive for the traffic pattern? Is the link partner implementing wake behavior poorly?
2
Physical Quality Symptom?
Check Layer 1 indicators and the channel itself. Measure insertion loss and return loss. Check cabling, connectors, and partner compatibility.
3
Frame Integrity Symptom?
Look at Layer 2 counters: FCS/CRC errors, alignment errors, giants, runts, and pause activity. Each one tells a different story.
4
Correlate the Layers
Rising FCS errors with poor return loss is a very different story from a clean physical channel with pause storms caused by downstream congestion.

## Slide 18
Six Misconceptions to Unlearn
X EEE just shuts the link off when idle
✓ It uses LPI, a managed cycle that preserves logical link continuity throughout.
X LPI means complete silence
✓ The quiet period is interrupted by refresh signals so the far end maintains timing and adaptive state.
X If the link is up, the PHY is healthy
✓ A link can be up while accumulating physical errors. L1 counters reveal that condition.
X FCS errors are a Layer 3 or app problem
✓ They are Ethernet-frame integrity failures pointing back to physical transport or link behavior.
X Insertion loss and return loss are the same
✓ Insertion loss is forward attenuation. Return loss is reflection from mismatch. Different causes, different fixes.
X Lower return loss is better
✓ Wrong direction. A higher return-loss value means less reflected signal, which is better.

## Slide 19
One Connected Story
Energy Efficient Ethernet
Links spend real time idle and can save power without pretending to go down
Low Power Idle
The managed state machine: Sleep, Quiet, Refresh, Wake — preserving receiver readiness
Layer 1 and 2 Counters
Operational evidence of whether signalling and frame delivery are actually healthy
Insertion and Return Loss
Core electrical reasons why healthy signalling either succeeds or fails
Stop treating network problems as isolated counters. Read them as symptoms of underlying link physics.