## Slide 1
802.1Q VLANs and Switch Internals
VLAN Tagging | Q-in-Q | Forwarding Database
Store-and-Forward vs Cut-Through | Switch Architecture
How does a switch decide what a frame means, where it belongs, and where it should go next?

## Slide 2
IEEE 802.1Q-2022: More Than Just a Tag
802.1Q is the base bridge-and-virtual-network standard for Ethernet. It specifies how bridges and switches segment traffic into virtual networks, learn device locations, forward or filter frames, and maintain orderly behavior across a multi-switch network.
802.1Q covers:
→ Classification of frames
→ Forwarding decisions
→ Filtering rules
→ VLAN and tag handling
→ Priority and QoS hints
→ Management and control
The right question to start with:
Not 'what does the tag look like?' but rather 'how does a switch decide what a frame means, which VLAN it belongs to, and where it should go next?'

## Slide 3
Why Ethernet Needed 802.1Q
A plain Ethernet LAN has no concept of multiple logical broadcast domains sharing one switching fabric. Without VLANs, broadcasts, unknown unicasts, and control effects spread everywhere.
Without VLANs
One flat Layer 2 domain
Broadcasts flood every port
No traffic isolation
All devices share one neighborhood
Security and performance suffer
With VLANs (802.1Q)
Multiple logical broadcast domains
Broadcasts contained within each VLAN
Controlled traffic isolation
Devices grouped by policy, not cable
Security and scale improve
A VLAN is not extra metadata. It is a rule for who is considered to be in the same Layer 2 neighborhood.

## Slide 4
Four Big Ideas Inside 802.1Q
The standard is best understood not as a tag format, but as four coordinated behaviors:
1
Classification
Deciding what VLAN and priority a received frame belongs to
2
Forwarding
Deciding where a frame should go based on MAC and VLAN context
3
Filtering
Deciding where a frame must NOT go to preserve VLAN separation
4
Control
Topology, tables, policy: the rules under which forwarding happens
The data plane carries out classification, forwarding, and filtering. The control plane sets the rules they operate by.

## Slide 5
The Basic Bridge Model
At its core, a switch is a bridge with multiple ports. Frames arrive on an ingress port, forwarding logic inspects them, and the switch decides: forward to one port, several ports, or none.
Port 1
Port 2
Port 3
Port 4
MAC RELAY
FDB Lookup
VLAN Filtering
Forwarding Decision
Port 5
Port 6
Port 7
Port 8
Forwarding is not just destination MAC. It is destination MAC in VLAN context. That is why VLAN support changes the bridge fundamentally.

## Slide 6
The VLAN Tag: Four Bytes in the Right Place
A tagged frame carries an extra four-byte field inserted between the source MAC address and the original EtherType. The receiver sees MAC addresses first, then immediately learns the VLAN context before deeper forwarding logic begins.
Dst MAC
Src MAC
TPID
81-00 or 88-A8
TCI
(VID+PCP+DEI)
EtherType / Length
Payload ...
802.1Q Tag (4 bytes inserted here)
TPID — Tag Protocol Identifier (2 bytes)
Tells the receiver a tag is present.
C-VLAN uses EtherType 0x81-00
S-VLAN uses EtherType 0x88-A8 (Q-in-Q)
TCI — Tag Control Information (2 bytes)
Carries VID (12 bits), PCP (3 bits), DEI (1 bit)
This is where VLAN identity, priority, and drop hints live

## Slide 7
Inside the Tag: VID, PCP, and DEI
VID
12 bits
VLAN Identifier
Range: 1 – 4094
Membership label, not a path. Tells the switch which logical Layer 2 domain this frame belongs to. The same MAC address can appear in different VLAN contexts, and must be treated separately.
PCP
3 bits
Priority Code Point
Range: 0 – 7
Bridges frame marking to internal queuing. A switch can map PCP values into different traffic classes and scheduling treatments — from best-effort to strict priority or credit-based shaping.
DEI
1 bit
Drop Eligible Indicator
Range: 0 or 1
Marks whether this frame may be dropped under congestion. A frame does not just claim VLAN membership; it also carries a hint about its own disposability if buffers fill up.

## Slide 8
Priority-Tagged Frames: A Special Case
A priority-tagged frame carries a VLAN tag with VID=0. It uses the tag purely to carry the PCP priority value, without asserting membership in a numbered VLAN. This is a detail that often confuses learners.
IEEE bridge management distinguishes three different admission policies at ingress:
Admit only
VLAN-tagged
Numbered VID present
Normal tagged frames
Admit only untagged
and priority-tagged
VID=0 or no tag
Priority info only
Admit all frames
All of the above
Most permissive setting
Why this matters operationally:
Tagged is not a single all-or-nothing bucket. The switch may treat ordinary VLAN-tagged and priority-tagged frames differently at ingress. This is why VLAN policy on an ingress port is more nuanced than it first appears.

## Slide 9
Q-in-Q: Tag Stacking Across Domains
Q-in-Q adds another 802.1Q-style tag around an already-tagged frame. The result is two stacked tags in a single Ethernet frame — each owned by a different administrative domain.
Dst MAC
Src MAC
S-VLAN Tag
88-A8 (outer)
C-VLAN Tag
81-00 (inner)
EtherType
Payload ...
Provider controls
Customer owns
Inner tag (C-VLAN, 0x81-00)
The customer's own VLAN context. Preserved intact across the provider network. The provider never needs to understand it.
Outer tag (S-VLAN, 0x88-A8)
The provider's transport context. The provider fabric forwards based on this tag, ignoring the customer's inner VLAN.

## Slide 10
Why Q-in-Q Solves the Provider Problem
Suppose two customers both use VLAN 100 internally. A provider cannot bridge both into one flat domain without losing their separation. Q-in-Q wraps each customer's traffic in a distinct outer service tag.
Customer A
VLAN 100
Provider Network
S-VLAN 200 | C-VLAN 100
S-VLAN 201 | C-VLAN 100
Customer B
VLAN 100
Customer A receives
original VLAN 100
Customer B receives
original VLAN 100
The key insight:
Outer tag = transport context (owned by provider). Inner tag = customer-local VLAN meaning (owned by customer). The two layers of meaning are completely independent — that is exactly why stacked tagging is powerful.

## Slide 11
Port Behaviors: How VLAN Identity Gets Assigned
Every frame needs a VLAN context when it enters the bridge. That context comes from one of two sources, depending on port configuration:
Port-Based Assignment (Access-style)
· Ingress port has a Port VLAN ID (PVID) configured
· Untagged incoming frames are stamped with that PVID
· VLAN identity is assigned by the port, not the frame
· Typical for end-device connections
Example:
An untagged frame from a workstation enters port 3. Port 3 has PVID 10. The switch internally treats it as belonging to VLAN 10.
Tag-Based Assignment (Trunk-style)
· The incoming frame already carries a VLAN tag
· The tag is read and becomes the VLAN context
· Port carries traffic for multiple VLANs simultaneously
· Typical for inter-switch or router links
Example:
A tagged frame arrives carrying VID 20. The bridge reads the tag and forwards within VLAN 20, with no need to add or override a PVID.

## Slide 12
Ingress Filtering: Enforcing Policy on the Way In
A switch does not have to accept every incoming tag pattern on every port. Ingress filtering allows the switch to enforce VLAN policy before a frame even enters the forwarding pipeline.
Frame
arrives
->
Acceptable
frame type?
->
VLAN permitted
on this port?
->
Forward
Reject: wrong
frame type
Reject: VLAN not
permitted here
Why this matters:
VLANs are not just an egress tagging trick. The switch enforces VLAN policy on ingress too. If a frame arrives with a VLAN context the port is not permitted to handle, it is dropped before it enters forwarding logic at all. This is why VLAN misconfiguration can produce mysterious silence rather than obvious errors.

## Slide 13
The Forwarding Database: The Switch's Memory
The FDB is the switch's memory of: where I last saw this source address in this VLAN context.
The FDB stores the information used by the forwarding process to decide through which ports frames should be forwarded. Without it, the switch would have to flood almost everything.
MAC Address
VLAN (VID)
Egress Port
Entry Type
Age
AA:BB:CC:DD:EE:01
10
GE0/1
Dynamic
12s
AA:BB:CC:DD:EE:02
10
GE0/2
Dynamic
48s
AA:BB:CC:DD:EE:03
20
GE0/1
Dynamic
5s
AA:BB:CC:DD:EE:04
10
GE0/4
Static
—
Note: the FDB is keyed by MAC address AND VLAN. The same MAC can appear in multiple VLANs as separate entries.

## Slide 14
MAC Learning: How It Works Step by Step
When a frame enters a switch, the source MAC address tells the bridge exactly where a device lives. This is the moment learning happens:
1
Frame arrives on port X in VLAN Y
The switch sees both source and destination MAC addresses on ingress
2
Record: source MAC S → port X, VLAN Y
The FDB is updated: if anyone needs to reach S, use port X within VLAN Y
3
Look up destination MAC D in FDB
Search FDB using D + VLAN Y as the combined key
4
Known D → forward to that port
Unicast to the single known egress port. No flooding needed.
5
Unknown D → flood within VLAN scope
Send to all ports permitted in VLAN Y except ingress. Flooding is the safe fallback.
The learning rule:
The switch learns from source addresses, not destinations. It can only know where to send traffic to a destination once that destination has been a source in some frame.

## Slide 15
VLAN Context Must Be Part of Learning
A VLAN-aware bridge does not learn in one flat universe. The same MAC address can genuinely exist in different VLAN contexts with different reachability.
IVL — Independent VLAN Learning
Each VLAN has its own independent FDB. The same MAC learned in VLAN 10 and VLAN 20 are stored as separate entries. Forwarding for each VLAN is fully isolated.
Default and most common in enterprise switches.
SVL — Shared VLAN Learning
A MAC address learned in one VLAN can be shared or visible across VLAN contexts, depending on bridge configuration. Reduces FDB memory use but sacrifices strict per-VLAN isolation.
Less common in modern deployments.
The FDB is not just keyed by MAC address. In a VLAN-aware world, the key is MAC address + VLAN context together.

## Slide 16
FDB Entries: Dynamic, Static, and Aging
Not all FDB entries are equal. The distinction between dynamic and static entries — and the role of aging — is fundamental to how a switch stays correct over time.
Dynamic Entries
· Learned automatically from observed source traffic
· Refreshed each time the source sends a new frame
· Expire after the aging timer (default: 300 seconds)
· Removed if the device goes silent or moves away
Static Entries
· Configured deliberately by an administrator
· Not dependent on traffic to remain valid
· Not subject to aging — persist until manually removed
· Used for critical infrastructure or security policy
Aging
· Prevents stale entries from misdirecting traffic
· A device that moves triggers flooding until re-learned
· Aging time is a tunable parameter
· Too short = unnecessary flooding; too long = stale paths
Aging is not optional housekeeping:
Without aging, a switch that once saw a device on port 3 would keep sending that device's traffic to port 3 forever — even after it moved to port 7, or disappeared entirely. Aging is what makes dynamic learning stay correct as the network changes.

## Slide 17
Unknown Destinations: Flooding as Safe Fallback
If a destination MAC has no FDB entry, the switch cannot confidently send to a single egress port. The safe and correct action is to flood within the allowed VLAN scope.
Learning and flooding are paired behaviors — they are not alternatives, they are complements:
Learning reduces future flooding
Once a source is seen, future traffic to that source as a destination can be unicast directly to the correct port
Flooding is the fallback when learning is incomplete
Unknown unicasts, multicast, and broadcast traffic must be spread within the VLAN until destination location is known
Key operational insight:
Flooding is not necessarily a fault. It is often the bridge's correct safe behavior when it does not yet know a precise destination location. A quiet network that suddenly generates wider traffic spread may simply have had an FDB entry age out, causing temporarily increased flooding until re-learning occurs.

## Slide 18
Store-and-Forward vs Cut-Through
The core question: does the switch wait for the entire frame before forwarding, or start as soon as it knows enough?
Store-and-Forward
Correctness first
· Receive entire frame into buffer first
· Validate frame integrity (CRC check)
· Then forward to egress port
· Handles speed mismatches gracefully
· Never propagates a known-bad frame
Cut-Through
Latency first
· Start forwarding as soon as header is parsed
· Do not wait for the frame tail or CRC
· Lower port-to-port latency, especially for large frames
· May forward frames that later prove corrupted
· Requires matching ingress and egress speeds
The real question in a live network is not which is universally better:
It is: what matters more here — the lowest possible forwarding latency, or stronger buffering, integrity checking, and congestion handling? Store-and-forward activates automatically when ingress rate exceeds egress port capacity.

## Slide 19
Cut-Through Is Not Forwarding After Six Bytes
A common misconception is that cut-through begins forwarding the instant the destination MAC address is read (6 bytes). The reality requires more:
Destination MAC
(6 bytes)
Source MAC
(6 bytes)
Outer VLAN tag
(4 bytes)
Inner tag if Q-in-Q
(4 bytes)
Enough context
for forwarding decision
Minimum needed before cut-through can safely begin forwarding on a VLAN-aware bridge ->
X Cut-through forwards after just 6 bytes (dest MAC)
✓ It forwards after enough header context to make a correct forwarding decision for the VLAN
X Cut-through never checks frame integrity
✓ It defers the check — bad frames may be partially or fully forwarded before the error is detected

## Slide 20
The Switch Pipeline: Not Just a Table Lookup
A switch is a pipeline of processing stages. Every frame passes through each stage in order — from receive to transmit.
Ingress Port
Logic
Receive frame
from medium
->
Parser /
Classifier
Detect tag, VLAN
context, priority
->
FDB
Lookup
Find destination
port + VLAN
->
Policy /
Filtering
Check VLAN,
ACLs, port rules
->
Buffering
& Queuing
S-and-F or
cut-through
->
Egress Port
Logic
Tag insert/remove
transmit frame
Data Plane
Executes the pipeline at line rate: receive, classify, look up, filter, queue, transmit. Decisions are made in real time per-frame.
Control Plane
Sets the rules: which VLANs exist, which ports participate, what policy applies. The data plane executes; the control plane decides.

## Slide 21
Control Plane vs Data Plane
The bridge architecture explicitly separates the control plane from the data plane. The data plane forwards frames in real time; the control plane determines the rules under which forwarding decisions are made.
Data Plane — executes
· Relay frames at line rate
· FDB lookup per frame
· Flood when destination unknown
· Apply per-port filtering rules
· Insert or remove VLAN tags
Control Plane — governs
· Which VLANs exist
· Which ports belong to which VLANs
· Topology-control method active
· Static forwarding or filtering policy
· Whether learning and flooding are permitted
The data plane can only be as correct as the control plane configuration that governs it.

## Slide 22
Six Misconceptions to Unlearn
X 802.1Q is only the four-byte VLAN tag format
✓ It specifies the full MAC bridge and VLAN bridge operation: classification, forwarding, filtering, and management.
X The VLAN ID alone tells the switch everything it needs
✓ The tag also carries PCP (priority) and DEI (drop eligibility), which map into internal queuing behavior.
X Q-in-Q is just two tags for no particular reason
✓ It separates customer VLAN context from provider transport context so both administrative domains coexist cleanly.
X The FDB is keyed only by MAC address
✓ In a VLAN-aware bridge, the key is MAC address plus VLAN context. The same MAC in two VLANs is two separate entries.
X Cut-through is always better because it is faster
✓ It is faster because it skips the CRC wait — but that means it may propagate corrupted frames store-and-forward would have dropped.
X Aging is just optional cleanup
✓ Aging prevents stale entries from permanently misdirecting traffic when devices move or disappear.

## Slide 23
The Complete Picture
IEEE 802.1Q-2022
The foundational standard for bridged Ethernet: classification, forwarding, filtering, and control.
VLAN Tagging (VID+PCP+DEI)
Four bytes that carry membership identity, priority hints, and drop eligibility — not just a VLAN number.
Q-in-Q Tag Stacking
Provider transport context wraps customer context so both domains coexist without collision.
Forwarding Database
The switch's per-VLAN, per-port memory of source addresses. Learning + aging = correct and current.
Store-and-Forward / Cut-Through
Two philosophies: wait for the full frame (correctness) or forward early (latency). Neither is universal.
Switch Pipeline
Receive → Classify → FDB Lookup → Filter → Queue → Transmit. Data plane executes; control plane governs.
A switch is not just a table lookup. It is a VLAN-aware, learning, aging, forwarding pipeline.