## Slide 1
Bridge Forwarding,
VLANs & Congestion
Forwarding · Filtering · Flooding | FDB & Learning
Priority, PCP, Traffic Classes | C-VLAN & S-VLAN
Classify → Learn → Look Up → Filter → Forward or Flood

## Slide 2
The Bridge's Real Job: Five Decisions per Frame
A switch is not just a box that sends packets onward. For every incoming frame it must answer at least four questions simultaneously:
Classify
What VLAN context
does this frame belong to?
->
Learn
Should the source
address be recorded?
->
Look Up
Is the destination
known in this VLAN?
->
Filter
Are any egress paths
forbidden?
->
Forward
or Flood
One port, many ports,
or no ports at all?
In a VLAN-aware bridge, forwarding decisions depend on destination MAC address AND VLAN tag together — not MAC alone.
The right mental model:
Not 'the switch looks up a MAC address' — but rather classify, then learn, then look up, then filter, then forward or flood. Each step depends on the one before it.

## Slide 3
Forward, Filter, Flood: Three Distinct Decisions
These three behaviors are not arbitrary. Each has a precise operational meaning and a specific trigger condition:
FORWARD
When the bridge knows the right egress port
The destination MAC is known in the VLAN context. The frame goes to exactly where it should — no more, no less.
FILTER
When the bridge knows a path is wrong or forbidden
The frame is intentionally blocked: wrong VLAN context on that port, port not in forwarding state, or policy-based rejection at ingress.
FLOOD
When the bridge does not know one correct destination
Unknown unicast, multicast with no matching entry, or broadcast. The frame is sent to all permitted ports in the VLAN scope — the safe discovery behavior.
Forward when you know the right place. Filter when you know a place is wrong. Flood when you do not yet know.

## Slide 4
Why Flooding Is Not a Sign of Failure
Flooding is the bridge's normal safe discovery behavior — not an error state. Understanding why requires understanding how learning works:
Device A sends
first frame to B
->
Bridge learns A
is on port X, VLAN Y
->
B unknown:
flood within VLAN
->
Device B replies
(now a source)
->
Bridge learns B
is on port Z, VLAN Y
After B replies → future traffic to B is unicast directly to port Z. Flooding stops.
Bridges learn from SOURCES
The bridge can only know where to deliver traffic to a destination once that destination has transmitted a frame as a source.
Flooding enables learning
Flooding a frame to all VLAN members is what gives the destination a chance to respond — and that response is what teaches the bridge.
Learning reduces future flooding
Once B is known, all subsequent traffic to B is unicast. Flooding is self-limiting: it creates the conditions for its own elimination.

## Slide 5
The Forwarding Database: Not Just a MAC Table
In a VLAN-aware bridge: Destination MAC + VLAN context → Forwarding/Filtering decision
The FDB is the bridge's memory of where it believes destinations are located. The standard's management model exposes: aging time, max FDB size, count of static entries, count of dynamic entries. Filtering entries carry both a MAC address and a set of VLAN identifiers.
Destination MAC
VLAN (VID)
Egress Port
Entry Type
Age
AA:BB:CC:11:22:33
10
GE0/2
Dynamic
22s
AA:BB:CC:44:55:66
10
GE0/5
Dynamic
91s
AA:BB:CC:77:88:99
20
GE0/2
Dynamic
4s
FF:FF:FF:FF:FF:FF
10
Flood all
Static
—
The same MAC address in two different VLANs = two separate FDB entries. Forwarding knowledge is always VLAN-scoped.

## Slide 6
Dynamic Learning, Static Entries, and Aging
The FDB can be populated in two fundamentally different ways, and one process keeps it honest over time:
Dynamic Entries
· Learned automatically from observed traffic
· Source MAC + port + VLAN recorded on arrival
· Refreshed by continued traffic from that source
· Expire after aging timer (default: 300 seconds)
Adaptive — follows the network as it changes
Static Entries
· Installed deliberately by an administrator
· Not derived from passive traffic observation
· Not subject to aging — persist until removed
· Used for policy, security, or critical infrastructure
Intentional — overrides automatic learning
Aging
· Removes dynamic entries after timeout period
· Prevents stale entries from persisting after device moves
· Traffic from the source refreshes the aging clock
· Too short = excess flooding; too long = stale paths
Correctness — keeps learned state believable
The key insight on aging:
Without aging, a bridge could keep sending traffic toward a port long after the device had moved, been unplugged, or reconnected elsewhere. Aging is what makes dynamic learning stay correct in a changing network — it is not cosmetic housekeeping.

## Slide 7
VLAN Relay: More Than Carrying a Tag
A VLAN-aware bridge is not relaying raw Ethernet in one flat universe. It is relaying frames within a specific VLAN context. Every step of the forwarding pipeline is VLAN-scoped:
1
Ingress port classifies into VLAN context
Via the frame's own tag, or via the port's PVID for untagged frames
2
Source address learned in that VLAN context
The FDB entry is: source MAC → port, specifically within this VLAN
3
Destination looked up in that VLAN context
FDB key is destination MAC + VLAN together, never MAC alone
4
Forwarding or flooding within VLAN scope
Only ports that are members of this VLAN are eligible egress destinations
5
Egress port tags or untags per port config
Whether the transmitted frame carries a tag depends on the egress port's role
VLAN relay is not just tag carriage. It is the whole pipeline of classifying, learning, forwarding, filtering, and flooding inside a chosen VLAN scope.

## Slide 8
Access and Trunk Ports: Operational Shorthand
Access and trunk are useful deployment terms — but they are not the deepest 802.1Q architectural concepts. The underlying bridge mechanisms are:
PVID — Port VLAN Identifier
Default VLAN assigned to untagged ingress frames. How access-port behavior is expressed in 802.1Q.
AFT — Acceptable Frame Types
Whether this port admits tagged-only, untagged+priority-tagged, or all frames.
IF — Ingress Filtering
Whether frames whose VLAN context is not permitted on this port are discarded on arrival.
ET — Egress Tagging
Whether frames leave this port tagged or untagged, and with what tag type.
Practical mapping:
Access style: untagged ingress mapped to PVID, egress sent untagged for that VLAN. Trunk style: multiple VLANs on one link, usually tagged, under explicit per-port admission rules.

## Slide 9
C-VLAN and S-VLAN: Two Tags, Two Roles
C-VLAN and S-VLAN do not just differ by a number. They differ in architectural role — who owns the VLAN meaning and what scope it controls:
C-VLAN (Customer VLAN)
EtherType: 0x81-00 Owner: Customer / enterprise side Role: Customer-local VLAN meaning Scope: Within customer's administrative domain
S-VLAN (Service VLAN)
EtherType: 0x88-A8 (from IEEE 802.1ad) Owner: Service provider side Role: Provider transport or service context Scope: Within provider's administrative domain
A Provider Bridge is built around a single S-VLAN component that can carry multiple C-VLAN meanings. The S-VLAN is the relay scope; the C-VLAN is the transported content.

## Slide 10
Q-in-Q: What the Outer Tag Really Controls
Dst MAC
Src MAC
S-VLAN
0x88-A8
(outer)
C-VLAN
0x81-00
(inner)
EtherType
Payload...
Provider forwards on outer tag
Customer meaning preserved
The problem Q-in-Q solves
Multiple customers may use the same VLAN IDs. Bridging both into one flat provider domain loses their separation. Q-in-Q wraps each customer in a distinct service tag.
How the outer tag works
The provider network learns and forwards on S-VLAN context. Broadcast, unknown unicast, and multicast flood within S-VLAN scope — not across all customers.
The inner tag is transparent
The inner C-VLAN rides untouched through the provider fabric. At the provider edge it is stripped away and delivered to the customer in its original form.

## Slide 11
Congestion Management: A Pipeline, Not Just Queues
Congestion management is what happens when too many eligible frames compete for the same egress resource. Under light load it is invisible. Under heavy load it is everything:
Decode
Priority
PCP from tag
or port default
->
Regenerate
Priority
Remap per-port
under policy
->
Map to
Traffic Class
Internal class
assignment
->
Transmission
Selection
Strict priority,
CBS, ETS...
->
DEI
Drop Policy
Who gets
dropped first
->
Egress
Transmit
Frame leaves
with new PCP
The better description of congestion management:
Not 'the switch has queues' — but a policy chain: decode priority from the tag, possibly regenerate or remap it, assign to a traffic class, apply a scheduling or shaping algorithm to decide service order, and use DEI to decide what may be sacrificed first under buffer pressure.

## Slide 12
Priority Regeneration: Wire Priority vs Bridge Priority
Priority regeneration is how the bridge says: the priority that arrived on the wire does not have to be the priority I use internally.
Wire priority
(from PCP field)
->
Priority
Regeneration
Table
(per port, per incoming priority)
->
Internal priority
(used for class lookup)
Different ingress contexts
A received priority 6 on port 1 (trusted uplink) may remain 6. The same value on port 8 (untrusted device) may be demoted to 2 before class lookup.
Domain boundary translation
Ports at the boundary of different priority conventions or administrative domains may need different regeneration rules to maintain consistent internal behavior.
Default: pass-through
The standard default is that regenerated priority equals received priority — so no regeneration unless the administrator configures a different mapping.

## Slide 13
PCP Decoding and Encoding: Not Just Pass-Through
PCP is not simply carried through the bridge untouched. 802.1Q defines both a decoding table and an encoding table at each bridge port:
Incoming
VLAN Tag
PCP 0-7
DEI 0/1
->
PCP
Decode Table
PCP + DEI ->
Internal priority + drop-eligible state
->
Priority
Regeneration
Remap per
port policy
->
Traffic Class
Mapping
Priority ->
Class 0-7
->
PCP
Encode Table
Internal priority ->
Outgoing PCP + DEI
->
Outgoing
VLAN Tag
New PCP
New DEI
Decode table: ingress
Maps incoming PCP (0-7) and DEI to internal priority and drop-eligible state. A PCP 5 frame on an untrusted port may decode to a lower internal priority.
Encode table: egress
Maps internal priority and drop-eligible state back to an outgoing PCP value and DEI bit. The outgoing PCP may differ from what arrived, by design.
Why this matters
Priority semantics can be preserved, translated, or normalized across networks. A bridge does not blindly carry the PCP bit — it may actively transform it.

## Slide 14
Traffic Classes and Transmission Selection
Having an internal priority is only the beginning. The bridge must then decide how that priority is served on egress — via a two-stage mapping:
Internal
Priority
(0 – 7)
->
Traffic Class
Table
Class 0 (lowest)
Class 1
Class 2
Class 3
Class 4
Class 5
Class 6
Class 7 (highest)
->
Transmission
Selection Algorithm
Strict Priority (SP)
Credit-Based Shaper (CBS)
Enhanced Transmission Select (ETS)
Asynchronous Traffic Shaping (ATS)
Under congestion, what matters: which class does the frame land in, and which algorithm serves that class.

## Slide 15
Drop Eligibility: Who Gets Sacrificed First
Congestion management is not only about who goes first. It is also about who may be sacrificed when buffers are under stress. That is what the DEI bit expresses:
DEI = 0:
Not drop-eligible. The bridge will protect this frame from discard under congestion.
DEI = 1:
Drop-eligible. Under buffer pressure, this frame may be discarded rather than transmitted.
DEI is set by the sender or by policy
A frame enters a network segment marked as drop-eligible by the originating device, or the bridge policy marks it based on metering (e.g., excess above contracted rate).
DEI interacts with PCP tables
The PCP decoding and encoding tables model the association between PCP, priority, and drop-eligible state — DEI is not an isolated bit, it is part of the priority-treatment pipeline.
drop-encoding config per port
Bridge port config specifies whether frames marked drop-eligible must be encodable on that port or else be discarded outright — giving operators fine-grained control.

## Slide 16
Access, Trunk, and VLAN Relay: The Complete View
Device
(untagged)
Access port
PVID=10
AFT: untagged
Egress: untagged
VLAN-AWARE
BRIDGE
Trunk port
PVID=1
AFT: tagged
VLAN 10,20,30
Uplink
(tagged)
Device
(untagged)
Access port
PVID=20
AFT: untagged
Egress: untagged
Trunk port
PVID=1
AFT: tagged
VLAN 10,20
To other
switch
In both cases the bridge does the same core job: classify into VLAN context, learn, look up, filter, and forward within scope.
The difference is only how VLAN context is supplied:
Access style: context supplied by the port's PVID configuration. Trunk style: context supplied by the explicit tag carried in the frame.

## Slide 17
C-VLAN and S-VLAN in the Provider Bridge
In a provider bridge, the S-VLAN is the relay scope. The C-VLAN is the transported content. Forwarding, filtering, and flooding happen in the S-VLAN domain:
Customer A
VLAN 100
Edge
Bridge A
Add S-VLAN
200 outer
Provider Core
(forwards on S-VLAN only)
Edge
Bridge Z
Strip S-VLAN
deliver C-VLAN
Core bridges: S-VLAN only
Provider core switches never inspect or modify the inner C-VLAN. They learn and forward purely on S-VLAN context.
Edge bridges: translate context
The provider edge bridge maps incoming customer traffic to an S-VLAN and strips it back on exit — the customer sees only their C-VLAN throughout.
BUM traffic scope is S-VLAN
Broadcast, unknown unicast, and multicast flood within S-VLAN scope — meaning traffic crosses customer boundaries only within the same service VLAN.

## Slide 18
Six Misconceptions to Unlearn
X Flooding is always bad
✓ Flooding is the bridge's normal fallback for unknown unicast and multicast before sufficient destination knowledge exists.
X The FDB is just a flat MAC table
✓ In a VLAN-aware bridge, forwarding entries are always tied to VLAN context — the key is MAC address plus VLAN, not MAC alone.
X Access and trunk are the deepest 802.1Q concepts
✓ They are operational shorthand. The actual mechanisms are PVID, acceptable frame types, ingress filtering, and egress tagging behavior.
X PCP just passes through the bridge unchanged
✓ The bridge can decode incoming PCP, regenerate priority, map to traffic classes, and then encode a different PCP on egress.
X Congestion management just means bigger buffers
✓ It is a policy chain: metering, priority regeneration, traffic-class mapping, scheduling or shaping algorithms, and DEI drop policy.
X S-VLAN and C-VLAN are just two names for the same thing
✓ C-VLAN (0x81-00) carries customer-side VLAN meaning. S-VLAN (0x88-A8) carries provider-side service context. Different EtherTypes, different roles.

## Slide 19
One Complete Picture
Forwarding Pipeline
Classify → Learn → Look Up → Filter → Forward or Flood. Every frame, every time, within VLAN scope.
FDB: MAC + VLAN = Decision
The FDB key is always destination MAC plus VLAN context. Dynamic entries learn and age; static entries persist by design.
Access, Trunk, VLAN Relay
Two ways to supply VLAN context: port-assigned (PVID) or tag-carried. The bridge does the same job either way.
C-VLAN and S-VLAN
Customer tags (0x81-00) carry customer meaning. Service tags (0x88-A8) carry provider transport context. Q-in-Q stacks both.
Congestion Management
PCP decode → priority regeneration → traffic class → transmission selection → DEI drop policy. Not just queues.
Drop Eligibility (DEI)
Frames may be marked sacrificeable under congestion, separate from their VLAN membership or priority level.
A frame arrives. The bridge classifies, learns, decides, and either delivers it precisely — or floods it safely until it can.