## Slide 1
SVL, IVL, Queuing
& Automotive VLANs
Shared vs Independent VLAN Learning | FIFO · SP · WRR · WFQ
Credit-Based Shaper | Management VLANs | Automotive Context
Classify into VLAN → but should MAC learning be shared or independent?

## Slide 2
VLAN-Aware Forwarding Raises a Learning Question
Once forwarding depends on both destination MAC address and VLAN tag together, the bridge must answer a deeper question about learning:
Do these VLANs represent independent Layer 2 attachment spaces —
or multiple traffic scopes over essentially the same learned attachment space?
Independent VLAN Learning (IVL)
Each VLAN has its own separate MAC learning table.
Same MAC in VLAN 10 and VLAN 20 = two separate entries.
The answer to: separate Layer 2 spaces
Shared VLAN Learning (SVL)
A selected set of VLANs shares one learned MAC-location view.
Learning in one VLAN can be used for forwarding in the others.
The answer to: shared attachment space
IEEE 802.1Q-2022 explicitly exposes ivl-capable, svl-capable, and hybrid-capable as separate bridge capabilities — this is a fundamental part of VLAN-aware bridging.

## Slide 3
IVL: Each VLAN Is Its Own MAC Universe
Under IVL, MAC learning is done independently for each VLAN context. The same MAC address can be learned on different ports in different VLANs without any conflict:
FDB — VLAN 10
AA:AA:AA:AA:AA:AA
Port 3
BB:BB:BB:BB:BB:BB
Port 1
CC:CC:CC:CC:CC:CC
Port 5
FDB — VLAN 20
AA:AA:AA:AA:AA:AA
Port 7
DD:DD:DD:DD:DD:DD
Port 2
EE:EE:EE:EE:EE:EE
Port 4
AA:AA:AA:AA:AA:AA → Port 3 in VLAN 10
AA:AA:AA:AA:AA:AA → Port 7 in VLAN 20
Same MAC — two separate, independent learned entries
The IVL mental model:
The switch treats each VLAN as having its own MAC-learning world. Virtualization, cloning, and device reuse mean the same MAC can legitimately appear in multiple VLANs without any forwarding ambiguity.

## Slide 4
SVL: A Set of VLANs Shares One Learning View
Under SVL, if a MAC address is learned in one VLAN, that information is used for forwarding decisions in all other VLANs in the same designated set:
Shared FDB — VLANs 10, 20, and 30 (SVL group)
AA:AA:AA:AA:AA:AA
Port 3
VLAN 10 (learned here)
BB:BB:BB:BB:BB:BB
Port 1
VLAN 20 (learned here)
CC:CC:CC:CC:CC:CC
Port 5
VLAN 10 (learned here)
Used for forwarding in ALL three VLANs in this SVL group
Efficient reuse
Learning the same endpoint in each VLAN separately is redundant when the underlying attachment space is the same. SVL avoids that duplication.
Scoped, not universal
SVL does not mean all VLANs everywhere share one table. It means a configured set of VLANs shares a learning domain — others remain independent.
Use with intention
SVL is useful in provider or transport designs where VLANs are distinct for policy or labeling reasons but do not represent separate reachability domains.

## Slide 5
IVL vs SVL: Choosing the Right Model
The choice is not aesthetic — it follows directly from what the VLANs actually represent in your design:
Question
IVL says...
SVL says...
Are VLANs separate broadcast and forwarding domains?
✓ IVL natural fit — each VLAN is its own universe
SVL would mix learning across intended boundaries
Can the same MAC legitimately exist in multiple VLANs?
✓ IVL handles this cleanly — separate FDB entries per VLAN
SVL could cause forwarding ambiguity
Are VLANs distinct in label but sharing an attachment space?
IVL would create redundant per-VLAN learning
✓ SVL avoids unnecessary duplication
Is this a provider/transport design with VLAN bundles?
IVL possible but less efficient here
✓ SVL is often the right fit
Default assumption when in doubt?
✓ IVL — IEEE model defaults ivl-capable = true
svl-capable defaults to false in 802.1Q model
Start with IVL. Reach for SVL only when VLANs are distinct in label but intentionally share one learned attachment space.

## Slide 6
Three Reasons VLANs Exist
Not all VLANs exist for the same reason. Understanding the purpose explains why SVL vs IVL matters at all:
1
Broadcast Domain Segmentation
One VLAN = one isolated broadcast domain on a shared switch fabric. Broadcasts, unknown unicasts, and multicast are contained within VLAN scope. This is the most fundamental use.
Purpose: isolation · IVL is the natural fit
2
Policy Separation
Even when topology is shared, different traffic groups get isolated for security, performance, or administrative reasons. Per-VLAN learning, filtering, and forwarding scope enforce those separations.
Purpose: access control · IVL again natural
3
Transport Context (C-VLAN / S-VLAN)
S-VLANs (EtherType 0x88-A8) carry C-VLANs (0x81-00) transparently through a provider network. Here VLANs are envelopes, not end-user domains — SVL can be appropriate.
Purpose: encapsulation · SVL may fit here
Why this connects to IVL vs SVL:
VLANs for isolation → IVL. VLANs for labeling or transport scoping over a shared topology → SVL may apply. The use case drives the learning model, not the other way around.

## Slide 7
Why Switches Need Queues at Egress
A switch does not need a queue only when the outgoing link is always instantly available.
Real links do not work that way:
Port 1
(ingress)
Port 2
(ingress)
Port 3
(ingress)
Egress Queues
Priority Class 7 (highest)
Priority Class 4
Priority Class 2
Priority Class 0 (lowest)
->
Egress
Port
The switch must decide:
1. Where to store frames temporarily
2. In what order to serve them
3. Which queues get more service
The switch is not just choosing which packet goes next. It is choosing a service discipline for a set of competing traffic classes.

## Slide 8
Four Queuing Policies: What Each One Promises
Each queuing discipline makes a different trade-off between simplicity, urgency, fairness, and determinism:
FIFO
First In, First Out
+ Simplest, lowest overhead
- Blind to traffic class — bulk traffic can crowd out critical traffic
Good baseline. Inadequate when traffic classes mix.
SP
Strict Priority
+ Minimizes latency for highest-priority class
- Lower-priority queues can starve under sustained load
Powerful for urgent traffic. Use carefully.
WRR
Weighted Round Robin
+ Proportional service share, no starvation
- Does not give hard deterministic guarantees — relative shares only
Good for 'all classes matter' designs.
WFQ
Weighted Fair Queuing
+ Fairness-oriented, protects low-volume interactive flows
- Not a named 802.1Q transmission-selection algorithm in bridge silicon
Excellent reference model, but not an 802.1Q knob.

## Slide 9
FIFO and Strict Priority: Two Extremes
FIFO — First In, First Out
Packets transmitted in order of arrival. No concept of priority or traffic classes.
✓ Simplest possible implementation
✓ Lowest processing overhead
✗ Blind to traffic importance
✗ Bursty sources crowd out critical traffic
✗ Inadequate when traffic classes mix
Strict Priority (SP)
Highest non-empty priority queue is always served before any lower-priority queue.
✓ Minimizes latency for top-priority class
✓ Simple and predictable urgency model
✓ Best for traffic that truly needs to go first
✗ Lower-priority queues can starve completely
✗ Dangerous if used without load analysis
FIFO ignores importance. SP maximizes importance. Neither handles the case where several classes all need reliable service.

## Slide 10
WRR and WFQ: Sharing Service Over Time
Weighted Round Robin (WRR)
Serves queues in turn, but each queue receives service proportional to its configured weight. If a queue is empty, the scheduler immediately moves on — no wasted turns.
Proportional bandwidth share
Intuition: Strict Priority asks who is most important right now. WRR asks how service should be shared over time. Good when several classes all matter.
No starvation. Proportional, not deterministic.
Weighted Fair Queuing (WFQ)
A fairness-oriented scheduling concept that divides bandwidth by weights and tries to protect low-volume interactive traffic from bulk flows.
Conceptually richer than WRR — it models weighted fair sharing among flows, not just queue turns.
Important caveat: IEEE 802.1Q does not name WFQ as one of its transmission-selection algorithms. The 802.1Q model names Strict Priority, Credit-Based Shaper, Enhanced Transmission Selection, and ATS.
WFQ is an excellent reference concept — but is not the standard 802.1Q scheduler knob you configure on bridge silicon.
Good reference model — not a named 802.1Q algorithm.

## Slide 11
Credit-Based Shaper: Beyond Priority Flags
Some traffic needs better delay and burst behavior than a pure scheduler can deliver — but it does not need a full time-triggered schedule. CBS fills that gap:
The problem CBS solves: time-sensitive streams must not bunch into large bursts that hurt their own latency — or the latency of others.
Priority alone is insufficient
Strict Priority tells a queue to go first, but it says nothing about how that queue releases frames over time. A burst of high-priority frames can still saturate the link at once.
CBS adds rate discipline
The Credit-Based Shaper allows a queue privileged treatment while also smoothing and rate-disciplining its transmission so frames are spread over time, not released all at once.
IEEE 802.1Qav origin
CBS was introduced in IEEE 802.1Qav for audio/video traffic that needed to use a high fraction of bandwidth while spacing frames out to reduce bursting and bunching.
CBS is a smoothing and rate-disciplining mechanism for a traffic class — not just a priority flag.

## Slide 12
How CBS Works: The Credit Wallet
CBS uses four parameters to govern when a traffic class may transmit. Think of it as a credit wallet:
idleSlope
Rate at which credit accumulates while the queue is waiting (has frames but is not transmitting)
sendSlope
Rate at which credit is depleted while the queue is actively transmitting frames
hiCredit
Maximum positive credit that can accumulate — caps how much a burst can be front-loaded
loCredit
Minimum credit (can go negative) — how deep in debt the queue can go before it must stop
The credit cycle:
Waiting: credit builds at idleSlope rate. Transmitting: credit depletes at sendSlope rate. Credit goes negative: queue pauses until credit recovers above zero. Result: smooth, rate-disciplined transmission rather than uncontrolled bursts.

## Slide 13
CBS vs Strict Priority: A Critical Distinction
Both give privileged treatment to a traffic class — but their behavioral guarantees are fundamentally different:
Strict Priority
If a high-priority queue is non-empty, always serve it first. No rate constraint. No smoothing. The queue can burst at full line rate as long as frames are waiting.
Protects: urgency (who goes first)
Leaves open: burst size, inter-frame spacing, instantaneous link saturation
Protects urgency only
Credit-Based Shaper (CBS)
This class may have privileged treatment, but it is also rate-disciplined by a credit algorithm. Transmission is spread out; the queue cannot burst uncontrollably even under sustained high load.
Protects: urgency AND controlled transmission pacing
Bounds: burst size, average service rate, inter-frame behavior
Protects urgency and tames burstiness
Strict Priority protects urgency. Credit-Based Shaper protects urgency while also taming burstiness. That is why 802.1Q treats CBS as a named algorithm in its own right.

## Slide 14
Management VLAN: What It Is and What It Is Not
A management VLAN is not a special 802.1Q tag type. It is an ordinary VLAN chosen by the operator to carry management-plane traffic.
What makes it management?
Not a special EtherType or flag in the tag. Simply the operator's policy choice to dedicate one VLAN to carrying SSH, SNMP, logging, and web control interfaces — and to not mix that with data traffic.
Control-plane isolation
If management traffic rides in its own VLAN, user or application VLANs do not automatically expose the switch's management interface. That alone reduces accidental exposure significantly.
Operational clarity
Troubleshooting and automation are simpler when the switch's management address belongs to a known dedicated VLAN, not whichever data VLAN happens to be nearby.
Typical management VLAN traffic:
· SSH remote access
· SNMP polling and traps
· Syslog / event logging
· Web UI / REST management
· NETCONF / YANG tooling
· Zero-touch provisioning
Important caution:
A management VLAN gives you traffic separation. It does not by itself guarantee secure management. You still need routing policy, authentication, and access control if the management VLAN spans multiple links or devices.

## Slide 15
Automotive VLANs: Separating Mixed-Criticality Traffic
Modern vehicles run many traffic types over a single Ethernet fabric. VLANs enforce the separation that safety and performance require:
Safety-Relevant Control
Engine, braking, steering control loops
IVL — must never share learning
Safety-Relevant Media
ADAS sensor streams, cameras, lidar, radar
IVL — perception isolation critical
Infotainment / Comfort
Audio/video, display, A/C, windows, lighting
IVL — isolate from safety domains
Diagnostics / Engineering
OBD-II, calibration, development logging, debug access
IVL or management VLAN
Management / Service
Switch management, ECU flashing, plant service tools
Dedicated management VLAN
The automotive VLAN purpose:
This is not departmental separation for convenience. These domains have genuinely different latency, reliability, and exposure requirements. A safety control loop must not be affected by an infotainment media burst. VLANs and queueing policy together enforce that boundary.

## Slide 16
IVL vs SVL in Automotive Networks
The same decision logic from data communications applies — but the stakes are higher when the traffic carries safety-relevant functions:
IVL — Default Automotive Choice
Most automotive VLANs exist precisely to separate functional domains with different criticality. An ADAS perception VLAN and an infotainment VLAN must not share forwarding context — their traffic is intended to be isolated.
IVL is the cleaner and safer interpretation for any VLAN that represents a true functional boundary.
IEEE 802.1Q capability defaults (ivl-capable = true) align with this automotive instinct.
Use when: domains must not share learned state
SVL — Specialized Automotive Use
SVL can be useful in engineered automotive backbones where several VLANs are meant to share the same learned attachment space while remaining distinguishable for policy or transport reasons.
Example: a backbone fabric where VLAN labels indicate traffic class or priority, but all classes reach the same endpoints through the same physical topology.
This is more specialized, but it is exactly why the standard supports both models.
Use when: VLANs differ in policy but share topology

## Slide 17
Queuing Policy Choices in Automotive
Map each traffic class to the least-complex queuing policy that still meets its behavior requirements:
Policy
Automotive Fit
Verdict
FIFO
Too weak for mixed criticality. Bulk infotainment can delay safety-critical frames.
Avoid for any traffic mix
Strict Priority
Ideal for safety control loops and ADAS streams that must go first under any load.
Use for highest-criticality classes
WRR
Good for multiple classes that all need reliable service — diagnostics, logging, comfort traffic.
Use for important non-critical classes
CBS
Ideal for time-sensitive streams like ADAS video and audio/video infotainment — rate-disciplines bursts while fitting TSN toolbox.
Use for bounded-latency streams
CBS and TSN shapers are especially valuable in automotive — bounded latency and controlled burstiness, not just rough prioritization.

## Slide 18
The Complete Picture
IVL
Each VLAN learns independently. The same MAC in two VLANs = two separate entries. Default for true functional separation.
SVL
A configured set of VLANs shares one learned MAC-location view. Use when VLANs are distinct in label but share one attachment space.
FIFO
Simple, blind, no priority. Adequate only on lightly loaded links with no traffic class differentiation needed.
Strict Priority
Top queue always goes first. Minimizes latency for critical traffic. Can starve lower classes under sustained load.
WRR
Serves queues by configured weight. Proportional service, no starvation. Good for several classes that all deserve bandwidth.
WFQ
Fairness-oriented scheduling concept. Excellent reference model. Not a named 802.1Q bridge transmission-selection algorithm.
CBS
Credit accumulates while waiting, depletes while sending. Rate-disciplines a traffic class to smooth bursts. A named 802.1Q TSN algorithm.
Management VLAN
An ordinary VLAN dedicated to device management traffic by policy. Not a special tag type. Gives isolation, not security by itself.
In automotive: VLANs and queuing policy together separate and protect traffic classes with different criticality over one shared Ethernet fabric.